## Slide 1: Harmonium: Asymmetric, Bandstitched UWB for Fast, Accurate, and Robust Indoor Localization
Benjamin Kempke Pat Pannuto Prabal Dutta University of Michigan
IPSN 2016

## Slide 2: What is Harmonium?
High-quality indoor localization
The CrazyFlie Nano
Fast (> 1 m/s), small (5 g payload), flying machine

## Slide 3: Harmonium tracks microquadrotors in real time with 14 cm accuracy

## Slide 4: How does Harmonium do it?
Time Difference of Arrival

## Slide 5: What makes Harmonium different?
Pushes most complexity from the node to localize to fixed infrastructure
  Tags are:
    Inexpensive
    Low-power
    Lightweight
Harmonium solves the shortcomings of current RF localization technologies
  Achieves high accuracy in multipath-rich environments
  Receiver uses well-studied traditional narrowband architecture
  Composed of only common, off-the-shelf components
Notes: High precision localization syst

## Slide 6: Why Bother with Indoor Localization Anyway?
Autonomous Robotics
Location Attestation
Asset Tracking
http://i.dailymail.co.uk/i/pix/2012/07/16/article-2174271-14150BDF000005DC-987_634x372.jpg
http://cdn.wonderfulengineering.com/wp-content/uploads/2013/06/Amazon-warehouse.jpg
https://farm2.staticflickr.com/1313/556806349_e38a6a2668_b_d.jpg
http://www.irobotweb.com/~/media/Images/iRobot/Robots/HRD/Roomba/600%20Series/Anatomy/irobot-roomba-600-sideview.jpg?h=397&la=en&w=663
http://i.cbc.ca/1.2447541.1385989501!/fileImage/httpImage/image.jpg_gen/derivatives/16x9_620/amazon-drone.jpg
Notes: Drone -> delivery drone
Attestation -> unlock office, pay for coffee

## Slide 7: Hasn’t indoor localization been done before? Why Harmonium?
Harmonium prioritizes
Location quality
Tag Simplicity
At the cost of anchor complexity
Notes: Smaller is better
Harmonium focuses on tag metrics and localization accuracy, where it excels

## Slide 8: So, how does Harmonium do it?
D?

## Slide 9: Harmonium measures the Time Difference of Arrival
Tag Send
D1
D2
D1 – D2

## Slide 10: Multilateration: Time-Difference-of-Arrival to Location

## Slide 11: Multilateration: Time-of-Arrival to Location

## Slide 12: In the real world, it is hard to accurately measure these distances

## Slide 13: IPSN’15 Microsoft Indoor Localization Competition: A strong indicator of localization performance
http://research.microsoft.com/en-US/events/indoorloccompetition2015/2015_indoorloc_competition_light.pptx
Notes: 2015 Localization Competition results
  Comparison: Accuracy vs. BW

## Slide 14: The majority of indoor localization systems use RF
http://research.microsoft.com/en-US/events/indoorloccompetition2015/2015_indoorloc_competition_light.pptx
Can operate in non-line-of sight
High speed
Moderate energy and cost
Notes: 2015 Localization Competition results
  Comparison: Accuracy vs. BW
Rewrite titles to make sense, thrown off otherwise

## Slide 15: And the best RF-based systems use Ultra-Wideband (UWB)
http://research.microsoft.com/en-US/events/indoorloccompetition2015/2015_indoorloc_competition_light.pptx
Notes: 2015 Localization Competition results
  Comparison: Accuracy vs. BW

## Slide 16: What is Ultra-Wideband?
Narrowband
Ultra-Wideband
5.31 GHz
5.33 GHz
5 GHz
6 GHz
Time Domain
Frequency Domain
Notes: Add in frequency domain duals

## Slide 17: Why does ultra-wideband give better range estimates?

## Slide 18: Why does ultra-wideband give better range estimates?

## Slide 19: If we want to use UWB today, what’s available?
Commercial RTLS
802.15.4a Transceiver (DecaWave)
TimeDomain P440
Ubisense Research Package
TimeDomain P330
Sewio
Pixie
OpenRTLS
Ciholas DWUSB
Redpoint Positioning
Pozyx

## Slide 20: What if we want to build our own UWB transmitter?
Major types
  High-Speed Comparators
  SRD-Based
  CMOS
  BJT-Based
Wentzloff, David D., and Anantha P. Chandrakasan. "Gaussian pulse generators for subbanded ultra-wideband transmitters." Microwave Theory and Techniques, IEEE Transactions on 54.4 (2006): 1647-1655.
Hantscher, Sebastian, et al. "Hardware concepts for the sequential sampling of repetitive pulse radar echoes in cost‐efficient ultra‐wideband transceivers."Microwave and Optical Technology Letters 52.3 (2010): 585-591.
Kim, Hyunseok, D. Park, and Y. Joo. "All-digital low-power CMOS pulse generator for UWB system." Electronics Letters 40.24 (2004): 1.
X
X

## Slide 21: Harmonium: The Architecture

## Slide 22: Harmonium: The Tag
Tag specs:
  Pure COTS design
  $4.50 in modest quantity
  75 mW active power
Concept of operation:
  BJT NPN Pulse generator
  Monoflop generator
  Pulse Repetition Frequency (PRF) generator
  Trigger filter
  Pulse-shaping filter

## Slide 23: Harmonium: The Tag
Notes: Notes: Uses ASE-4.000MHZ-LC-T (+/- 50 ppm)

## Slide 24: Harmonium: The Tag

## Slide 25: Harmonium: The Tag

## Slide 26: Harmonium: The Tag

## Slide 27: Harmonium: The Tag

## Slide 28: Harmonium Tag: The Need for Filtering
Pulse w/o filtering  Pulse w/ trigger filtering  Pulse w/ shaping filter

## Slide 29: Harmonium Tag: The Need for Filtering
Pulse w/o filtering  Pulse w/ trigger filtering

## Slide 30: Harmonium Tag: The Need for Filtering
Pulse w/o filtering  Pulse w/ trigger filtering

## Slide 31: Harmonium Tag: The Need for Filtering
Pulse w/o filtering  Pulse w/ trigger filtering  Pulse w/ shaping filter

## Slide 32: How to measure the time of arrival of pulses from the tag?

## Slide 33: Commercial UWB receivers expect standard packets and modulation

## Slide 34: UWB receivers from research are too expensive, noisy, or niche
UWB Receivers
  High-Speed ADCs
  Energy detection receivers
  Sampling Receivers
Hantscher, Sebastian, et al. "Hardware concepts for the sequential sampling of repetitive pulse radar echoes in cost‐efficient ultra‐wideband transceivers."Microwave and Optical Technology Letters 52.3 (2010): 585-591.
Segura, Marcelo, et al. "Experimental demonstration of self-localized ultra wideband indoor mobile robot navigation system." Indoor Positioning and Indoor Navigation (IPIN), 2010 International Conference on. IEEE, 2010.
Rabbachin, Alberto, et al. "UWB energy detection in the presence of multiple narrowband interferers." Ultra-Wideband, 2007. ICUWB 2007. IEEE International Conference on. IEEE, 2007.
X
X
X

## Slide 35: In the real-world, UWB is not alone
http://www.theiet.org/resources/journals/eletters/4811/images/640_uwb-spectrum2.jpg

## Slide 36: Harmonium: UWB Reception with Narrowband Radios
Concept of operation:
  Generic narrowband receiver
  Frequency-swept local oscillator
  Antenna diversity

## Slide 37: Harmonium: UWB Reception with Narrowband Radios
Concept of operation:
  Generic narrowband receiver
  Frequency-swept local oscillator
  Antenna diversity

## Slide 38: Harmonium: UWB Reception with Narrowband Radios
Concept of operation:
  Generic narrowband receiver
  Frequency-swept local oscillator
  Antenna diversity

## Slide 39: Harmonium: UWB Reception with Narrowband Radios
Concept of operation:
  Generic narrowband receiver
  Frequency-swept local oscillator
  Antenna diversity

## Slide 40: Harmonium: UWB Reception with Narrowband Radios
Concept of operation:
  Generic narrowband receiver
  Frequency-swept local oscillator
  Antenna diversity

## Slide 41: Harmonium: UWB Reception with Narrowband Radios
Concept of operation:
  Generic narrowband receiver
  Frequency-swept local oscillator
  Antenna diversity

## Slide 42: Harmonium reconstructing UWB signals in the real world

## Slide 43: Time-Domain Representation to Time-of-Arrival

## Slide 44: How well does Harmonium actually work?
Experiment #1: Stationary Accuracy
Experiment #2:
Mobile Localization Accuracy
Experiment #3:
Mobile Localization (Reproducibility)

## Slide 45: Experimental Evaluation #1: Stationary Accuracy
Stationary, Unobstructed
Stationary, Obstructed
14 cm median error
16 cm median error

## Slide 46: Commercial UWB receivers fail in the presence of narrowband interferers
Spectrum is becoming increasingly crowded
UWB fails with modest narrowband interference
DW1000 Datasheet

## Slide 47: Harmonium still able to achieve accurate location estimates in the presence of narrowband interference
28 cm median error
Notes: Technique used: “Robust Uncertainty Principles: Exact Signal Reconstruction from Highly Incomplete Frequency Information” (Convex optimization problem)

## Slide 48: Experimental Evaluation #2: Tracking Micro-Quadrotors
14 cm median error
46 cm 95%ile error
Up to 1.4 m/s
19 Hz sampling

## Slide 49: Future Extensions
Digital Communication
Multi-tag support

## Slide 50: Conclusions
Harmonium introduces novel UWB transmitters, receivers, and signal processing techniques
Harmonium increases anchor complexity to realize minimal tags
1.5 cm3, 75 mW, 3 g
Harmonium is a robust, high-precision indoor localization technology
14 cm median error
16 cm median error “through “the walls”
28 cm median error in the face of narrowband interference
Ben Kempke, Pat Pannuto, and Prabal Dutta

## Slide 51: Backup Slides

## Slide 52: The Disadvantages of UWB Reception with Narrowband Receivers
Maximum attainable update rate goes down proportional to the number of required observations
More complex signal processing required to reconstruct wideband channel representation