## Slide 1: SurePoint: Exploiting Ultra Wideband Flooding and Diversity to Provide Robust, High-Fidelity Indoor Localization
Electrical Engineering & Computer Science University of Michigan
Benjamin Kempke Pat Pannuto Bradford Campbell Prabal Dutta

## Slide 2: SurePoint: An Ultra-Wideband RF Localization System
SurePoint: a localization platform achieving high localization accuracy
  50% within 17 cm, 95% within 76 cm
  Enabled by commercially-available UWB
  The Problem: Commodity UWB is a new technology with a number of limitations in its real-world implementation
    Provide location abstraction, not a radio interface
?

## Slide 3: Highly accurate (RF-based) indoor localization technology has arrived
Time
Accuracy (m)
1999
10.00
1.00
0.01
0.10
WASP [‘11/0.50]
2002
2005
2008
2011
2014
2017
Harmonia [‘14/0.40], RF-IDraw [‘14/0.38]
Tagoram [‘14/0.12], WiTrack [‘14/0.12]
PolyPoint [‘15/0.31]
Harmonium [‘16/0.09]
LANDMARC [‘04/2.00]
WREN [‘13/2.00]
Cricket [‘00/0.10]
Dolphin [‘04/0.24]
3D-LOCUS [‘09/<0.01]
iBadge [‘02/0.10]
Salathé [‘10/2.00]
Social fMRI [‘11/5.00]
RADAR[‘00/2.94]
Opo [‘14/0.05]
SurePoint [‘16/0.29]

## Slide 4: Why Does Ultra-Wideband Yield Better Localization Performance?

## Slide 5: Why Does Ultra-Wideband Yield Better Localization Performance?

## Slide 6: UWB: A Performant Technology with Significant Limitations
Robustness
Regulatory-limited Transmit Power
Scalability
Modularity

## Slide 7: PolyPoint RF Localization System
X
X

## Slide 8: The Need for Diversity In the Presence of Line-of-Sight
802.15.4a Channel Model: Molisch, Andreas F., et al. "IEEE 802.15. 4a channel model-final report." IEEE P802 15.04 (2004): 0662.

## Slide 9: The Need for Diversity Measurements
27 different observations of the RF channel
  3 tag antennas * 3 anchor antennas * 3 RF channels
12th percentile of range estimates used
  yields zero-mean distribution of error in LoS environments
Median ranging error:
  17 cm to 8 cm
95th percentile ranging error:
  65 cm to 34 cm

## Slide 10: Ranging Error Stationarity
Range Error
?

## Slide 11: Ranging Error Stationarity
Range Error
Range Error
?

## Slide 12: Measuring Range Using Two-Way Time-of-Flight
time →
?

## Slide 13: Efficiently Leveraging Diversity
time →
?
M = # of measurements

## Slide 14: Efficiently Leveraging Diversity
time →
O(2*N*M) packets
Example: 2*4*27 = 216 packets  5 Hz
N = # of anchors
M = # of measurements
?
?

## Slide 15: Efficiently Leveraging Diversity
time →
N = # of anchors
M = # of measurements
?
?

## Slide 16: Efficiently Leveraging Diversity
time →
O((N+1)*M) packets
Example: (4+1)*27 = 135 packets  7 Hz
N = # of anchors
M = # of measurements
?
?

## Slide 17: Efficiently Leveraging Diversity
time →
O(N+M) packets
Example: 4+27 = 31 packets  32 Hz
N = # of anchors
M = # of measurements
?
?

## Slide 18: UWB: A Performant Technology with Significant Limitations
Robustness
Regulatory-limited Transmit Power
Scalability
Antenna Diversity
Ultra-Wideband Flooding
Lightweight Scheduling & Synchronization
SurePoint

## Slide 19: Addressing Scalability: Scheduling and Network Messaging with Glossy Floods
Adopted Low-Power Wireless Bus (LWB):
  All data communicated using Glossy floods
  Host schedules time slots for localization and flooding intervals
  Incoming tags request to be scheduled during a ‘contention’ period
  Outgoing tags either request to be unassigned or time out
  Steady state operation: All tags scheduled with an even assignment of timeslots to tags

## Slide 20: Adopting Glossy Concepts for Network Flooding and Time Synchronization
Glossy: Flooding with constructive narrowband interference
  Allows for a robust means of broadcasting a single message to all nodes in the network
Narrowband
UWB
+

## Slide 21: Extending Flooding to UWB: Multipath = Constructive Interference
0
1
2
3
4
5
0
1
2
3
4
5
+

## Slide 22: UWB Flooding Condition: Time Synchronization
Necessary condition:
Transmitter synchronization must be better than symbol time (preamble: 1 μs, data: 128 ns)
How it’s done:
Recurring flooding transmission times based on received flood timestamp
0
1
2
3
4
5
0
1
2
3
4
5
X

## Slide 23: UWB Flooding Condition: Carrier Synchronization
Necessary condition:
Transmitter carriers must maintain coherence during flood packet transmission
How it’s done:
Crystal tuning continuously adapted based on inter-sync interval
0
1
2
3
4
5
0
1
2
3
4
5

## Slide 24: UWB: A Performant Technology with Significant Limitations
Robustness
Regulatory-limited Transmit Power
Scalability
Modularity
Antenna Diversity
Ultra-Wideband Flooding
Lightweight Scheduling & Synchronization
TriPoint Module
SurePoint

## Slide 25: SurePoint’s TriPoint Module
  Integrated module providing localization abstraction
    I2C interface
    STM32 MCU for protocol orchestration
    DecaWave DW1000 UWB transceiver
    Calculates ToAs of incoming packets
Triangular shape  Supports antenna diversity
?
Two-Way
Time-of-Flight
Time Difference of Arrival

## Slide 26: Conclusion
Overcoming shortfalls of UWB localization to make deployable systems targeting a wide spectrum of potential applications
SurePoint:
  Decimeter-level localization accuracy
    Worst-case performance enhanced with diversity
  Network-wide communication, scheduling, and synchronization
    Scheduling with UWB flooding for reliable, network-wide communication
  Localization abstraction, modular architecture to ease adoption
  Performance to enable a variety of localization applications
    17 cm median 3D error
    95% within 76 cm
Ben Kempke

## Slide 27: Questions?
Benjamin Kempke Pat Pannuto Bradford Campbell Prabal Dutta

## Slide 28: Backup Slides

## Slide 29: Extending Flooding to UWB: CIR Superposition = Constructive Interference
Intensity
Time (ns)

## Slide 30: IPSN’15 Microsoft Indoor Localization Competition: A strong indicator of localization performance
http://research.microsoft.com/en-US/events/indoorloccompetition2015/2015_indoorloc_competition_light.pptx

## Slide 31: And the best RF-based systems use Ultra-Wideband (UWB)
http://research.microsoft.com/en-US/events/indoorloccompetition2015/2015_indoorloc_competition_light.pptx

## Slide 32: Efficiently Leveraging Diversity
O(2*N*M) packets
Example: 2*3*27 = 162 packets  6 Hz
N = # of anchors
M = # of measurements

## Slide 33: Efficiently Leveraging Diversity
O((N+1)*M) packets
Example: 4*27 = 108 packets  9 Hz
N = # of anchors
M = # of measurements

## Slide 34: Efficiently Leveraging Diversity
O(N + M) packets
Example: 3 + 27 = 30 packets  33 Hz
N = # of anchors
M = # of measurements

## Slide 35: Efficiently Leveraging Diversity
Minimum: 2*N packets
N = # of anchors

## Slide 36: Efficiently Leveraging Diversity
Minimum: N+1 packets
N = # of anchors

## Slide 37: Extending Flooding to UWB: Further Reach with Simultaneous Transmissions

## Slide 38: Efficiently Leveraging Diversity
A total of 27 different combinations:
  tag antenna (3)
  anchor antenna (3)
  UWB channels (3)
Full 2-way message exchange is too costly (27 * 4 * 2 = 216 packets)
Modified ranging protocol pares this down to a total of 34 required packets
  27 broadcast one-way ranging packets
  N (>4) unicast anchor  tag packets

## Slide 39: Ultra-Wideband (UWB): The Burgeoning Choice for Indoor Localization
Narrowband
Ultra-Wideband
5.31 GHz
5.33 GHz
5 GHz
6 GHz
Time Domain
Frequency Domain

## Slide 40: SurePoint Performance Assessment
17 cm median 3D error
95% of estimates within 76 cm
No noticeable degradation in the presence of fast tag movement (2.4 m/s)
<1 Watt active power