## Slide 1: Lessons From Five Years of Making Michigan Micro Motes (M3)
Pat Pannuto, Yoonmyung Lee, ZhiYoong Foo, Gyouho Kim, David Blaauw, and Prabal Dutta
University of Michigan
6th Workshop on Architectural Research Prototyping (WARP ‘15)
June 14, Portland, Oregon, USA

## Slide 2: Behind the scenes on what was required to realize an ecosystem of mm-scale computers
On display now at the computer history museum

## Slide 3: 2008: The Phoenix Processor
World’s lowest power computer
  Set records for volume and energy
  And could be used by at best the grad students that built it
The Phoenix Processor: A 30pW Platform for Sensor Applications, M. Seok, VLSI ‘08
Mingoo Seok
Scott Hanson
Yu-Shiang Lin
ZhiYoong Foo
Daeyeon Kim
Yoonmyung Lee
Nurrachman Liu
Dennis Sylvester
David Blaauw
Notes: Phoenix: Mingoo Seok, Scott Hanson, Yu-Shiang Lin, Zhiyoong Foo, Daeyeon Kim, Yoonmyung Lee, Nurrachman Liu, Dennis Sylvester, David Blaauw
IOP: Gregory Chen, Hassan Ghaed, Razi-ul Haque, Michael Wieckowski, Yejoong Kim, Gyouho Kim, David Fick, Daeyeon Kim, Mingoo Seok, Kensall Wise, David Blaauw, Dennis Sylvester

## Slide 4: From temperature sensor to pressure sensor: 3 Years.
Motivating application for mm-scale sensor: Intraocular pressure
  Critical diagnostic tool for glaucoma
A Cubic-Millimeter Energy-Autonomous Wireless Intraocular Pressure Monitor, G. Chen, ISSCC ‘11
2 mm
1.2 mm
0.7 mm
Notes: http://blaauw.eecs.umich.edu/getFile.php?id=434&sid=vomuvflatyhha
IoP – 1.2 mm wide, 2 mm long, 0.7 mm high, 0.35 mm high battery

## Slide 5: What’s wrong with this picture: “How to build a wireless temperature sensor?”
Step 1: Buy a low-power temperature sensor
Step 1: Design a low-power temperature sensor
~10 pW standby, < 1 µW active
cm-scale
mm-scale

## Slide 6: What’s wrong with this picture: “How to build a wireless temperature sensor?”
Step 1: Buy a low-power temperature sensor
Step 2: Buy a low-power microcontroller
Step 1: Design a mm-scale temperature sensor
Step 2: Design a mm-scale CPU
~10 pW standby, < 1 µW active
cm-scale
mm-scale

## Slide 7: What’s wrong with this picture: “How to build a wireless temperature sensor?”
Step 1: Buy a low-power temperature sensor
Step 2: Buy a low-power microcontroller
Step 3: Add low-power communications
Step 1: Design a mm-scale temperature sensor
Step 2: Design a mm-scale CPU
Step 3: Design a mm-scale radio
~10 pW standby, ~5 µW active
mm-scale
cm-scale

## Slide 8: What’s wrong with this picture: “How to build a wireless temperature sensor?”
Step 1: Buy a low-power temperature sensor
Step 2: Buy a low-power microcontroller
Step 3: Add low-power communications
Step 4: Add a power supply
Step 1: Design a mm-scale temperature sensor
Step 2: Design a mm-scale CPU
Step 3: Design a mm-scale radio
Step 4: Add power supply and storage
Energy Harvesting
Energy Storage
mm-scale
cm-scale

## Slide 9: What’s wrong with this picture: “How to build a wireless temperature sensor?”
Step 1: Buy a low-power temperature sensor
Step 2: Buy a low-power microcontroller
Step 3: Add low-power communications
Step 4: Add a power supply
Step 5: Integrate the chips
Step 1: Design a mm-scale temperature sensor
Step 2: Design a mm-scale CPU
Step 3: Design a mm-scale radio
Step 4: Add power supply and storage
Step 5: Integrate the modules
mm-scale
cm-scale

## Slide 10: What’s wrong with this picture: “How to build a wireless temperature sensor?”
Step 1: Buy a low-power temperature sensor
Step 2: Buy a low-power microcontroller
Step 3: Add low-power communications
Step 4: Add a power supply
Step 5: Integrate the chips
Step 1: Design a mm-scale temperature sensor
Step 2: Design a mm-scale CPU
Step 3: Design a mm-scale radio
Step 4: Add power supply and storage
Step 5: Integrate the modules
mm-scale – Monolithic System
cm-scale – Modular System

## Slide 11: What’s wrong with this picture: “How to build a wireless temperature sensor?”
Integrate components using well-defined, standard interfaces
  SPI
  UART
  I2C
Integrate components using Verilog
  temp_sense t1 (
    …
    .sample_valid_out (to_proc_t1_sample_valid),
    .sample_out (to_proc_t1_sample),
    );
  processor p1 (
    …
    .temp_valid_in (to_proc_t1_sample_valid),
    .temp_in (to_proc_t1_sample),
What’s different?
mm-scale – Monolithic System
cm-scale – Modular System

## Slide 12: What’s wrong with this picture: “How to build a wireless temperature sensor?”
Integrate components using well-defined, standard interfaces
  SPI
  UART
  I2C
Previously unseen constraints on volume and energy
mm-scale – Monolithic System
cm-scale – Modular System

## Slide 13: What’s wrong with this picture: “How to build a wireless temperature sensor?”
Integrate components using well-defined, standard interfaces
  SPI
  UART
  I2C
mm-scale – Monolithic System
cm-scale – Modular System
Previously unseen constraints on volume and energy

## Slide 14: What’s wrong with this picture: “How to build a wireless temperature sensor?”
Integrate components using well-defined, standard interfaces
  SPI
  UART
  I2C
mm-scale – “Modular” Systems
cm-scale – Modular System
Ad-hoc composition results in poor use of volumetric space

## Slide 15: MBus, the missing interconnect that enables the mm-scale computing class
22.6 pJ / bit / chip, < 10 pW standby / chip
Single-ended (push-pull) logic
Low, fixed wire count (4)
Multi-master
Power-aware
Implemented in over a dozen (and growing) mm-scale chips
  CPU, Radio
  Flash Memory
  Temperature, Pressure, Imager
To make half a dozen (and growing) mm-scale systems

## Slide 16: MBus enabled modular components, key to the rapid development cycle we now enjoy
2 uAh Battery
5 uAh Battery
Decap
Control/
PMU
Temp Sensor
Radio
+ CDC
Motion Detection/ Imager
Pressure Sensing
Temp. Sensing
MEMS
P. Sensor
Visual Sensing
From temperature sensor to pressure sensor:
3 months.
Notes: Modularity is one of the most important things in arch; when useful integrate. Currently mm-scale systems prematurely integrate due to artificial constraints

## Slide 17: Learn more about MBus at ISCA
Session 10B
  MBus: An Ultra-Low Power Interconnect Bus for Next Generation Nanopower Systems
Wednesday, 13:50 in Oregon 204

## Slide 18: Digging into what a mm-scale system looks like and why that really matters
Flashy pictures from a good camera can be misleading.
In practice, several nodes fit on a period

## Slide 19: How do you bootstrap (program) a node that’s too small to attach wires to?
Visible light communications
Gyouho Kim, Yoonmyung Lee, Suyoung Bang, Inhee Lee, Yejonng Kim, Dennis Sylvester, David Blaauw, “A 695 pW Standby Power Optical Wake-up Receiver for Wireless Sensor Nodes,” IEEE Custom Integrated Circuits Conference (CICC), September 2012
Notes: Orally mention other fresh-of-the-line issues, e.g. when the battery is connected

## Slide 20: Open Q: How do you debug a node that’s too small to attach wires to?
Partial answers
  Breakout system
  Visible light debugging
    Inject arbitrary messages
  Power trace debugging
    Each state has a power signature
  Bus snooping
    Plug-in for Saleae logic analyzer
Big Open Q: Postmortem

## Slide 21: [Recent efforts] How do you solder a node that’s too small to attach wires to?
Integrating mm-scale chips with COTS chips
Recent issues: Metals for both soldering and wirebonding
(to 50 μm pads)

## Slide 22: Re-discovering packaging problems from the MEMS community
Bio-compatible pressure sensor
  Can seal electronics in bio-compatible epoxy
  How to expose the pressure sensor?

## Slide 23: And adding some new packaging problems of our own
Bio-compatible pressure sensor
  Can seal electronics in bio-compatible epoxy
  How to expose the pressure sensor?
  Some of the electronics are light sensitive

## Slide 24: Systems considerations fit into the packaging puzzle too
Bio-compatible pressure sensor
  Can seal electronics in bio-compatible epoxy
  How to expose the pressure sensor?
  Some of the electronics are light sensitive
  The node relies on solar (or IR) harvesting to charge [and program…]

## Slide 25: How do you reliably manufacture a mm-scale system?
Most systems are “stair-step” stack of chips
Thin wafers (300  150 microns) [now brittle]
Then dice on die-attach film
Then flip onto stack and wirebond
Each step requires some learning…

## Slide 26: How do you reliably design a mm-scale system?
Conceptually simple: Turn off what you aren’t using
In practice, lots of diagrams that look like this:
Which represents only this corner of the chip

## Slide 27: Clock-gating != Power-gating. Need to eliminate static leakage as well
What is this diagram actually showing?
  Three hierarchical power domains
  Power control signals between domains
  Isolation gates between domains
Absence of tool support is biggest challenge
  Isolation correctness validated by hand
  Effects of isolation simulated “by hand”
    Often not at all
Always-on
Controlled
by green
Controlled
by red
Notes: “Off means off”

## Slide 28: How to bring a new chip into M3 ecosystem?
R1: Dedicated test chip
  Lots of I/O, scan, etc
Mohammad Hassan Ghaed, Skylar Skrzyniarz, David Blaauw, Dennis Sylvester, “A 1.6nJ/bit, 19.9µA Peak Current Fully Integrated 2.5mm2 Inductive Transceiver for Volume-Constraned Microsystems,” IEEE Custom Integrated Circuits Conference (CICC), September 2014
R2: Integrate
  Add MBus frontend
  Remove most debug pins, expose via registers
R3+: Bugs!

## Slide 29: There is a natural tension between building working systems and working chips
Need to avoid designing “modular” chips that only work in one system

## Slide 30: MPQ: A protocol standard for register and memory access brings SOC efficiency to multi-chip systems
Architectural shift: Remove CPU from steady-state operation
  Pre-programmed commands:
    ADC: “Every 128 samples, send DMA to radio”
    RF: “On DMA CH1 event, send buffer as payload of PKT_TEMPLATE_1”
  Atmel’s “sleepwalking”, TI’s μDMA controller
Traditional SOC
CPU
ADC
I2C
SPI
Sensor
Radio
SOCs:
Efficiency demands pushing designs back to a monolithic architecture
But the extensible parts aren’t efficient!
CPU can’t program sensor to send packet

## Slide 31: MPQ: A protocol standard for register and memory access brings SOC efficiency to multi-chip systems
Architectural shift: Remove CPU from steady-state operation
  Pre-programmed commands:
    ADC: “Every 128 samples, send DMA to radio”
    RF: “On DMA CH1 event, send buffer as payload of PKT_TEMPLATE_1”
  Atmel’s “sleepwalking”, TI’s μDMA controller
Traditional SOC
CPU
ADC
I2C
SPI
Sensor
Radio
The issue isn’t the physical layer

## Slide 32: The clean break of a new bus is an opportunity to standardize basic constructs
MPQ – “For those who mind their P’s & Q’s on MBus”
  Does not specify device behavior, command interface, etc
  Only specifies
    What a “register” looks like
    What “memory” looks like
    And how to read and write registers and memory
This is enough to enable powerful system synthesis constructs
And aligns with how systems are already designed today
MPQ

## Slide 33: MBus and MPQ are available today: mbus.io
“MBus Compatible”
  Logo certification
Specification and Verilog available (free forever)
MBus + MPQ: Standard interface for mm-scale components

## Slide 34: It takes a village…
2008
2009
2010
2011
2012
2013
2014
2015
2007
Mingoo Seok
Scott Hanson
Yu-Shiang Lin
ZhiYoong Foo
Daeyeon Kim
Yoonmyung Lee
Nurrachman Liu
Dennis Sylvester
David Blaauw
Gregory Chen
Mohammad
Hassan Ghaed
Razi-ul Haque
Michael Wieckowski
Yejoong Kim
Gyouho Kim
Prabal Dutta
Inhee Lee
Suyoung Bang
Dongmin Yoon
Ye-Sheng Kuo
Benjamin Kempke
Wanyeong Jung
Yen-Po Chen
Seokhyeon Jeong
Myungjoon Choi
Ronald Dreslinski
Pat Pannuto
David Wentzloff
Elnaz Ansari
Hyeongseok Kim
Kuo-Ken Huang
Ryan Rogel
Jonathan Brown
Notes: Phoenix: Mingoo Seok, Scott Hanson, Yu-Shiang Lin, Zhiyoong Foo, Daeyeon Kim, Yoonmyung Lee, Nurrachman Liu, Dennis Sylvester, David Blaauw
IOP: Gregory Chen, Hassan Ghaed, Razi-ul Haque, Michael Wieckowski, Yejoong Kim, Gyouho Kim, David Fick, Daeyeon Kim, Mingoo Seok, Kensall Wise, David Blaauw, Dennis Sylvester
JSSC: Yoonmyung Lee, Suyoung Bang, Inhee Lee, Yejoong Kim, Gyouho Kim, Mohammad Hassan Ghaed, Pat Pannuto, Prabal Dutta, Dennis Sylvester, and David Blaauw
IOT Design Space: David Blaauw, Dennis Sylvester, Prabal Dutta, Yoonmyung Lee, Inhee Lee, Sechang Bang, Yejoong Kim, Gyouho Kim, Pat Pannuto, Ye-Sheng Kuo, Dongmin Yoon, Wanyeong Jung, Zhi Yoong Foo, Yen-Po Chen, Jeong Seok-Hyeon, and Myungjoon Choi
VLSI Imager: Gyouho Kim, Zhi Yoong Foo, Pat Pannuto, Ye-Sheng Kuo, Benjamin Kempke, Mohammad Hassan Ghaed, Suyoung Bang, Inhee Lee, Yejoong Kim, Seokhyeon Jeong, Prabal Dutta, Dennis Sylvester, and David Blaauw
CICC: Ye-Sheng Kuo, Pat Pannuto, Gyouho Kim, Zhi Yoong Foo, Inhee Lee, Benjamin Kempke, Prabal Dutta, David Blaauw, and Yoonmyung Lee
Mbus: Pat Pannuto, Yoonmyung Lee, Ye-Sheng Kuo, ZhiYoong Foo, Benjamin Kempke, Gyouho Kim, Ronald G Dreslinski, David Blaauw, and Prabal Dutta