## Slide 1: MBus An Ultra-Low Power Interconnect for Next Generation Nanopower Systems
Pat Pannuto, Yoonmung Lee, Ye-Sheng Kuo, ZhiYoong Foo, Benjamin Kempke, Gyouho Kim, Ronald G. Dreslinski, David Blaauw, and Prabal Dutta
University of Michigan
The 42nd International Symposium on Computer Architecture (ISCA’15)
June 13-17, Portland, Oregon, USA

## Slide 2: Bell’s Law: A new computing class every decade
Size (mm3)
Graphic originally from Dennis Sylvester
Laptop
1 per Company
1 per Professional
1 per Engineer
1 per Family
1 per Enterprise
1 per person
Corollary:
100x smaller / decade
“Smart Dust” should arrive by ~2017

## Slide 3: We have a diverse array of mm-scale components
Y.-S. Lin ‘08
V. Ekanayake ‘04
B. Warneke ‘04
CPUs
Communication
A. Ricci ‘09
J. Brown ‘13
M. Crepaldi ‘10
P. Chu ‘97
M. Scott ‘03
S. Hanson ‘09
Y.-S. Lin ‘07
ADCs and Sensors
Y. Lee ‘13
Timers
N. Sturcken ‘13
Power Management

## Slide 4: And a few mm-scale systems…
B. Warneke ‘07
The 1cc Computer
T. Nakagawa ‘08
Smart Dust
Y. Shapira ‘08
Smart Dew

## Slide 5: But where is the next class of computing?
Size (mm3)
Graphic originally from Dennis Sylvester
Smartphone
1 per Company
Laptop
1 per Professional
1 per Engineer
1 per Family
1 per Enterprise
1 per person
100 – 1000’s per person
?

## Slide 6: MBus is the missing interconnect that enables the mm-scale computing class
22.6 pJ / bit / chip, < 10 pW standby / chip
Single-ended (push-pull) logic
Low, fixed wire count (4)
Multi-master
Power-aware
Implemented in over a dozen (and growing) mm-scale chips
  CPU, Radio
  Flash Memory
  Temperature, Pressure, Imager
To make half a dozen (and growing) mm-scale systems

## Slide 7: Modularity is key for fast, iterative design, but was previously absent from mm-scale systems
Phoenix 2008:
  World’s lowest power computer
  Basically a temperature sensor
The Phoenix Processor: A 30pW Platform for Sensor Applications, Mingoo Seok, Scott Hanson, Yu-Shiang Lin, Zhiyoong Foo, Daeyeon Kim, Yoonmyung Lee, Nurrachman Liu, Dennis Sylvester, David Blaauw , VLSI ‘08
A Cubic-Millimeter Energy-Autonomous Wireless Intraocular Pressure Monitor, Gregory Chen, Hassan Ghaed, Razi-ul Haque, Michael Wieckowski, Yejoong Kim, Gyouho Kim, David Fick, Daeyeon Kim, Mingoo Seok, Kensall Wise, David Blaauw, Dennis Sylvester, ISSCC ‘11
Intraocular Pressure 2011:
  Collaboration for glaucoma health
  A pressure sensor
From mm-scale temperature sensor to mm-scale pressure sensor took 3 years

## Slide 8: MBus enables a modular, composable ecosystem of mm-scale components
2 uAh Battery
5 uAh Battery
Decap
Control/
PMU
Temp Sensor
Radio
+ CDC
Motion Detection/ Imager
Pressure Sensing
Temp. Sensing
MEMS
P. Sensor
Visual Sensing
From temperature sensor to pressure sensor:
3 months.
Notes: Modularity is one of the most important things in arch; when useful integrate. Currently mm-scale systems prematurely integrate due to artificial constraints

## Slide 9: Existing interconnects have served us well for 30 years. What makes mm-scale systems unique?
Node volume is dominated by energy storage
And volume is shrinking cubically
Battery
“Phone”
Batteries
“Sensor”
Battery
“Sensor”
10’s μW active, 10’s nW sleep, DC 0.1%

## Slide 10: Existing interconnects have served us well for 30 years. What makes mm-scale systems unique?
10’s μW active, 10’s nW sleep, DC 0.1%
Node volume is dominated by energy storage
And volume is shrinking cubically
I/O pads begin to account for non-trivial percentage of node surface area
Battery
“Phone”
Batteries
“Sensor”
Battery
“Sensor”
1 mm = 1,000 μm
50 μm, minimum viable bond pad
16-20 maximum I/O pins for 3D stacking

## Slide 11: SPI and I2C are like the USB and Firewire of embedded interconnects
Nearly every microcontroller has both
Nearly every peripheral has one or the other
Very few use anything else
  (except maybe UART)

## Slide 12: What is wrong with how are systems composed today?
SPI, invented by Motorola in ~1979
One master, N slaves
Shared clock: SCLK
Shared data bus: MOSI
Shared data bus: MISO
One Slave Select line per slave
Key Properties
    One dedicated I/O line per slave
  Master controls all communication
SCLK
MOSI
MISO
SS
Slave 1
SCLK
MOSI
MISO
SS
Slave 2
SCLK
MOSI
MISO
SS0
SS1
…
Master
Notes: Extremely populare; almost all MCUs have this interface

## Slide 13: What is wrong with how are systems composed today?
SPI, invented by Motorola in ~1979
One master, N slaves
Shared clock: SCLK
Shared data bus: MOSI
Shared data bus: MISO
One Slave Select line per slave
One interrupt line per slave
Key Properties
    One Two dedicated I/O lines per slave
  Master controls all communication
    Interrupts must be out-of-band
SCLK
MOSI
MISO
SS
INT
Slave 1
SCLK
MOSI
MISO
SS
INT
Slave 2
SCLK
MOSI
MISO
SS0
SS1
…
GPIO0
GPIO1
…
Master

## Slide 14: SPI’s I/O overhead and centralized architecture do not scale to mm-scale systems
SPI, invented by Motorola in ~1979
One master, N slaves
Shared clock: SCLK
Shared data bus: MOSI
Shared data bus: MISO
One Slave Select line per slave
One interrupt line per slave
Key Properties
    One Two dedicated I/O lines per slave
  Master controls all communication
    Interrupts must be out-of-band
SCLK
MOSI
MISO
SS
INT
Slave 1
SCLK
MOSI
MISO
SS
INT
Slave 2
SCK
MOSI
MISO
SS0
SS1
…
GPIO0
GPIO1
…
Master

## Slide 15: I2C has fixed I/O requirements and a decentralized architecture
I2C, invented by Phillips in 1982
  Any-to-(m)any on one shared bus
Key Properties
  Fixed wire count (2)
SCL
SDA
Node1
SCL
SDA
Node3
SCL
SDA
Node2

## Slide 16: I2C has fixed I/O requirements and a decentralized architecture
I2C, invented by Phillips in 1982
  Any-to-(m)any on one shared bus
Key Properties
  Fixed wire count (2)
  Open-collector
    Multi-master
    Flow Control
SCL
SDA
Node1
SCL
SDA
Node3
SCL
SDA
Node2
Open-collector (aka wired-AND)

## Slide 17: The problem is the energy costs of running an open-collector
Send a “1”: 0 J
VDD = 1.2 V
Send a “0”: 174 pJ
@400 kHz
80% VDD as 1
R = 15.5 kΩ
(“the best”)
No setup, no hold

## Slide 18: The problem is the energy costs of running an open-collector
Send a “1”: 0 J
VDD = 1.2 V
R = 15.5 kΩ
(“the best”)
Send a “0”: 174 pJ
SCL Alone: 70 μW
@400 kHz
80% VDD as 1
@400 kHz
No setup, no hold
Bigger R?

## Slide 19: The problem is the energy costs of running an open-collector
Send a “1”: 0 J
VDD = 1.2 V
Send a “0”: 174 pJ
SCL Alone: 70 μW
@400 kHz
80% VDD as 1
@400 kHz
~ 3.1 mm
Two batteries
Active Energy Budget: 20 μW
Not an arbitrary number:
  Volume Target
  Lifetime Target
R = 15.5 kΩ
(“the best”)
No setup, no hold

## Slide 20: The energy demands of open-collectors make them unsuitable for mm-scale systems
SCL Alone: 70 μW
~ 3.1 mm
Two batteries
Active Energy Budget: 20 μW
Not an arbitrary number:
  Volume Target
  Lifetime Target
@400 kHz
Notes: Design for 20, try to hit 40 in practice

## Slide 21: Can we modify I2C to bring energy costs in line with mm-scale?
SCL
SDA
Master
SCL
SDA
Slave2
SCL
SDA
Slave1

## Slide 22: Replace the passive pull-up resistor with active circuitry
The Good : Able to achieve 88 pJ / bit (measured)
The Bad : Required clocks running at 5x bus clock on every chip
A Modular 1 mm3 Die-Stacked Sensing Platform with Low Power I2C Inter-die Communication and Multi-Modal Energy Harvesting
Yoonmyung Lee, Suyoung Bang, Inhee Lee, Yejoong Kim, Gyouho Kim, Mohammed Hassan Ghaed, Pat Pannuto, Prabal Dutta, Dennis Sylvester, David Blaauw
IEEE Journal of Solid-State Circuits

## Slide 23: Replace the passive pull-up resistor with active circuitry
The Good : Able to achieve 88 pJ / bit (measured)
The Bad : Required clocks running at 5x bus clock on every chip
The Bad : “I2C-like” is not I2C – required FPGA to integrate with COTS chips
The Ugly : Hand-tuned, ratioed logic on every chip – Not synthesizable
Ultra-Constrained Sensor Platform Interfacing
Pat Pannuto, Yoonmyung Lee, Benjamin Kempke, Dennis Sylvester, David Blaauw, and Prabal Dutta
IPSN 2012 (Demo)

## Slide 24: “Dark silicon” is more like “dimly lit silicon”
Clock-gated modules still exhibit static leakage
  Blows mm-scale power budget
mm-scale systems perform power-gating
  This means modules are cold-booting all the time
Manageable for monolithic designs because something always powered on
CPU
Sensor
Flash
Radio
Timer

## Slide 25: Modular mm-scale components introduce novel circuits problems and novel systems problems
CPU
Sensor
Flash
Radio
Timer
Clockless cold boot circuits are tricky
How do you know what’s awake?
How do you communicate with “pitch black” silicon to wake it up?
  I2C-variant: custom “wakeup” signal

## Slide 26: The MBus design follows from a careful consideration of all the requirements for modular, mm-scale systems
MBus Mediator
MBus Member
MBus Member
MBus Member
MBus Member
Clock
Data
Ring Topology
2 lines – 4 I/O per node
  Clock
  Data
“Shoot-Through”
CLK_IN
CLK_OUT

## Slide 27: To be extensible and respect I/O constraints, wire count must be independent of node count
MBus Mediator
MBus Member
MBus Member
MBus Member
Clock
Data
Recall SPI:
MBus Member

## Slide 28: Supporting interrupts with a fixed number of single-ended connections requires an arbitration protocol
Recall: “shoot through”
C wants to send a message
  Stop forwarding, drive 0
The mediator does not forward during arbitration
  Also generates the bus clock
MBus Mediator
A
B
D
C
Clock
Data
DATA_IN
DATA_OUT
1
1
1
1
1
1
1
1
1
1
0
0
0
0
1
1
Arbitrate

## Slide 29: Supporting interrupts with a fixed number of single-ended connections requires an arbitration protocol
Recall: “shoot through”
C wants to send a message
  Stop forwarding, drive 0
The mediator does not forward during arbitration
  Also generates the bus clock
MBus Mediator
A
B
D
C
Clock
Data
DATA_IN
DATA_OUT
1
1
1
1
1
1
1
1
1
1
0
0
0
1
1
0
0
0
0
0
0
Arbitrate

## Slide 30: Supporting interrupts with a fixed number of single-ended connections requires an arbitration protocol
What changes if B tries to send as well as C?
  B and C drive DATA_OUT to 0
B’s DATA_IN high, wins
C’s DATA_IN low, loses
MBus has topological priority
MBus Mediator
A
B
D
C
Clock
Data
1
1
1
1
1
1
1
1
1
1
0
0
0
0
1
1
0
0
0
0
0
0
0
1
Arbitrate
Notes: Transition: Now that we know who’s talking, how does the node declare who it’s talking to?

## Slide 31: Tradeoff between globally unique addresses, address length, and overhead
Embed addresses in message frames
  Overhead proportional to number of uniquely addressable device
I2C uses 7-bit device addresses with design-time LSBs
Requires I/O not available
Makes packaging assumptions
  mm-scale systems not always PCB
  Routing may not be easy
    3D stack
    Flip-chip + TSVs
Arbitrate
Address

## Slide 32: Tradeoff between globally unique addresses, address length, and overhead
3 Options
  Short static addresses and allow device conflicts
  Long static addresses to avoid device conflicts
  Non-static addresses
MBus does all 3
  4-bit: Static short prefixes (device class)
  24-bit: Static long prefixes (unique device ID)
  4-bit: Runtime enumeration protocol (replaces short prefix)
Arbitrate
Address
Notes: Mention broadcast messages orally

## Slide 33: Unbounded messages maximize flexibility and minimize overhead
An MBus message is 0…N bytes of data
Embed length in message
  Imposes large overhead for short messages
  Forces fragmentation of long messages
“End-of-message” sentinel byte(s)
  Imposes large overhead for short messages
  Requires escaping if sentinel is in transmitted
  Data-dependent behavior, hard to reason about
    Worst case 2x overhead!
Arbitrate
Data
Address

## Slide 34: MBus “interjections” provide an in-band end-of-message with minimal overhead
Data
During normal operation, Data toggles slower than Clock
Arbitrate
Interject
Data
Address
Clock
Data

## Slide 35: MBus “interjections” provide an in-band end-of-message with minimal overhead
During normal operation, Data toggles slower than Clock
Clock
Data
Arbitrate
Interject
Data
Address

## Slide 36: MBus “interjections” provide an in-band end-of-message with minimal overhead
During normal operation, Data toggles slower than Clock
Clock
Data
ACK
Idle
Arbitrate
Interject
Data
Address
control

## Slide 37: Transaction-level ACKs minimize common-case overhead while interjections preserve flow control
9 bytes
Arbitration
+
Address
+
Interjection
Arbitrate
Interject
Data
Address
control

## Slide 38: The modularity enabled by MBus created a circuits problem and a systems problem
Clockless cold boot circuits are tricky
How do you communicate with “pitch black” silicon to wake it up?
  How do you know what’s awake?
A power-gated node cannot send
  Use arbitration edges to drive the cold-boot circuitry
    (Minimal frontend: 35 gates, 4 regs)
  Nodes awaken before addressing
Nodes appear to be “always on”
  No need to know or track power states
MBus Mediator
MBus Member
MBus Member
MBus Member
Clock
Data
CPU
Sensor
Flash
Radio
Timer
Arbitrate
Interject
Data
Address
control

## Slide 39: These primitives enable an architectural shift in system design
CPU acts as configurator instead of overseer
  Preprogram temperature sensor to send radio packets
  Not unlike modern SOCs (sleepwalking, μDMA), but distributed
Sensor
Radio
CPU
Sensor
Radio
CPU

## Slide 40: Seamless and transparent interaction between power-aware and power-oblivious chips
Facilitates integration with COTS chips
*No current COTS chip support MBus, these integrations leverage more traditional buses still

## Slide 41: The majority of interconnect research is focused on performance at the expense of power and area
Chart: 
| RS232 Serial | Parallel (EPP) | Parallel (ECP) | USB 1.1 | USB 2.0 | USB 3.0
Throughput (MB) | 115 | 1000 | 5000 | 12000 | 48000 | 50000
5 Gb/s
115 b/s
43.5 million times faster
Chart: 
| ISA | PCI | Serial ATA 1.0 | AGP 2.0 (4x) | Sata 3.2 | PCIx 4.0 x16
Throughput (MB/s) | 22.8 | 125.8 | 150 | 1066 | 16000 | 31510
22.8 MB/s
31.5 GB/s
1,381
times faster

## Slide 42: Specification and Verilog at http://mbus.io
2 uAh Battery
5 uAh Battery
Decap
Control/
PMU
Temp Sensor
Radio
+ CDC
Motion Detection/ Imager
Pressure Sensing
Temp. Sensing
MEMS
P. Sensor
Visual Sensing

## Slide 43: MBus-based smart dust now on display at the computer history museum

## Slide 44: Protocol Overhead and message length

## Slide 45: Energy per bit of goodput (useful data)

## Slide 46: Power Draw Comparison

## Slide 47: Goodput of parallel MBus

## Slide 48: Saturating Transaction Rate

## Slide 49: Adding additional nodes does not have significant impact on MBus latency
MBus Mediator
MBus Member
MBus Member
MBus Member
Clock
Data
MBus Member
Recall: “shoot through”
DATA_IN
DATA_OUT
1
1
10 ns
~7 MHz
10 ns

## Slide 50: Some low-hanging fruit…
Full Duplex is trivial
“Selectively parallel”

## Slide 51: Arbitration Detail

## Slide 52: Interjection Detail

## Slide 53: Tertiary node power-on request

## Slide 54: Hierarchical Power Domains

## Slide 55: Implementation