## Slide 1: Ultra-Wideband and Indoor Localization
Pat Pannuto
In collaboration with Benjamin Kempke, Bradford Campbell, and Prabal Dutta
HotWireless’16
October 3, 2016, NYC, NY, USA
Notes: [as submitted in advance]:
Title: PolyPoint and the First Steps Towards Ubiquitous Location
Abstract: In the not too distant future, location will be a fundamental primitive available to all devices, akin to a unique id, a sense of time, and basic communication. This talk briefly articulates why location is a natural and inevitable primitive, explores the definition of a location, and considers the state and evolution of localization technology today. The talk then introduces the PolyPoint localization platform, an up-and-coming drop-in module that aims to provide high-fidelity indoor location information.

## Slide 2: Early RF-only localization (largely RSSI) had comparatively poor accuracy
Time
Accuracy (m)
1999
10.00
1.00
0.01
0.10
2002
2005
2008
2011
2014
2017
LANDMARC [‘04/2.00]
Cricket [‘00/0.10]
Dolphin [‘04/0.24]
iBadge [‘02/0.10]
RADAR[‘00/2.94]
Ultrasonic
(or UL+RF)
RF-Based
2002
  FCC allows unlicensed use of UWB spectrum
2005
  International UWB regulations
2007
  IEEE 802.15.4a

## Slide 3: What is Ultra-Wideband?
Narrowband
Ultra-Wideband
5.31 GHz
5.33 GHz
5 GHz
6 GHz
Time Domain
Frequency Domain
Notes: Add in frequency domain duals

## Slide 4: Indoors, reflections make time-of-flight estimation difficult and inaccurate

## Slide 5: UWB can better disambiguate multipath and identify signal arrival time

## Slide 6: Highly accurate (RF-based) indoor localization technology has arrived
Time
Accuracy (m)
1999
10.00
1.00
0.01
0.10
WASP [‘11/0.50]
2002
2005
2008
2011
2014
2017
Harmonia [‘14/0.40], RF-IDraw [‘14/0.38]
Tagoram [‘14/0.12], WiTrack [‘14/0.12]
PolyPoint [‘15/0.31]
Harmonium [‘16/0.09]
LANDMARC [‘04/2.00]
WREN [‘13/2.00]
Cricket [‘00/0.10]
Dolphin [‘04/0.24]
3D-LOCUS [‘09/<0.01]
iBadge [‘02/0.10]
Salathé [‘10/2.00]
Social fMRI [‘11/5.00]
RADAR[‘00/2.94]
Opo [‘14/0.05]
SurePoint [‘16/0.29]

## Slide 7: UWB technologies have driven success in high-fidelity RF-based localization
UWB-Based
2015
2016
UWB-based entries beginning to dominate IPSN localization competition
Half of competing teams achieved sub-meter accuracy
Takeaway: accuracy is a “solved” problem
D. Lymberopoulos, J. Liu, X. Yang, A. Naguib, A. Rowe, N. Trigoni, and N. Moayeri. Microsoft Indoor Localization Competition – IPSN 2015.
D. Lymberopoulos, J. Liu, Y. Zhang, P. Dutta, X. Yang, A. Rowe, V. Dequeira. Microsoft Indoor Localization Competition – IPSN 2016.

## Slide 8: Accuracy is only one facet of localization, and has reached “good enough”
Here are 12 dimensions
  Covering 9 technologies
    Each have several implementations
  (bigger is better) 
No one technology will fit all applications
  What does it mean to localize a person to 1cm?
  Motion? Walls? More??
Notes: Radar plot doesn’t even show through walls!

## Slide 9: This talk: New UWB-based systems that go beyond accuracy
(Though, all are highly [10-30 cm] accurate)
SurePoint [SenSys’16]
  Robust, scalable, and reliable
    53 cm 99th percentile error
Harmonium [IPSN’16]
  Inexpensive, low-power, lightweight
    Localizes quadcopters with 5 g payload limit
Slocalization [in progress]
  Lowest power and massively scalable

## Slide 10: SurePoint: Time-of-Flight between symmetric tag and anchor nodes

## Slide 11: PolyPoint showed how to make commercial UWB accurate, SurePoint makes it usable
PolyPoint/SurePoint key innovations:
  Exploit UWB channel diversity
  ^Efficiently with a broadcast-based ranging protocol
  UWB constructive interference to schedule and scale
PolyPoint: Guiding Indoor Quadrotors with Ultra-Wideband Localization (HotWireless’15)
SurePoint: Exploiting Ultra Wideband Flooding and Diversity to Provide Robust, Scalable, High-Fidelity Indoor Localization (SenSys’16)
Benjamin Kempke, Pat Pannuto, Bradford Campbell, and Prabal Dutta

## Slide 12: PolyPoint taught us that the UWB channel exhibits high variance
PolyPoint: Guiding Indoor Quadrotors with Ultra-Wideband Localization (HotWireless’15)
SurePoint: Exploiting Ultra Wideband Flooding and Diversity to Provide Robust, Scalable, High-Fidelity Indoor Localization (SenSys’16)
Benjamin Kempke, Pat Pannuto, Bradford Campbell, and Prabal Dutta
Channel model
Empirical Study
12th %ile Estimate
27 Samples  1 Range

## Slide 13: Broadcasts can make diversity acquisition efficient, but must also be robust
Naïve implementation: 27x3xN packets
PolyPoint: 27+1+N packets
3 anchors:
243 packets (~4 Hz)
3 anchors:
31 packets (~32 Hz)
SurePoint: 27+3+N packets
3 anchors:
33 packets (~31 Hz)
Problem:
In an open 20x20 m room with 16 anchors, PolyPoint ranges with an average of 4 each round
In the same room, SurePoint ranges with 7.3 of 9 deployed anchors
Notes: Mention where 3 comes from (N)
20 Hz number needs to be here – (naïve system gets XYZ Hz)

## Slide 14: Localizing multiple devices requires coordination to avoid interference
Insight: Borrow scheduling from sensor networking
  State of the art relies on constructive interference – UWB friendly?
PolyPoint: Guiding Indoor Quadrotors with Ultra-Wideband Localization (HotWireless’15)
SurePoint: Exploiting Ultra Wideband Flooding and Diversity to Provide Robust, Scalable, High-Fidelity Indoor Localization (SenSys’16)
Benjamin Kempke, Pat Pannuto, Bradford Campbell, and Prabal Dutta
A
I
B
New Tradeoffs:
Number of tags vs. update rate
Join latency vs. update rate

## Slide 15: Robust, accurate localization and best-in-class long-tail performance
Stationary Experiment
  7,500 samples
  0.29 m median error
  0.77 m 99th percentile error
  1.53 m worst case error
    0.76 m with 3-point median filter
  Recovered range in every eligible round
PolyPoint: Guiding Indoor Quadrotors with Ultra-Wideband Localization (HotWireless’15)
SurePoint: Exploiting Ultra Wideband Flooding and Diversity to Provide Robust, Scalable, High-Fidelity Indoor Localization (SenSys’16)
Benjamin Kempke, Pat Pannuto, Bradford Campbell, and Prabal Dutta

## Slide 16: SurePoint Today: Providing localization as a drop-in, modular primitive
TriPoint
Drop-in localization module
Towards “where-am-I” as an I2C command
TriTag
Carrier board
Adds BLE for offloading position information
PolyPoint: Guiding Indoor Quadrotors with Ultra-Wideband Localization (HotWireless’15)
SurePoint: Exploiting Ultra Wideband Flooding and Diversity to Provide Robust, Scalable, High-Fidelity Indoor Localization (SenSys’16)
Benjamin Kempke, Pat Pannuto, Bradford Campbell, and Prabal Dutta

## Slide 17: SurePoint design is limited by the use of a commercial UWB transceiver
Economic cost
  ~$10 at quantity 1,000
Energy cost
  280 mW
Flexibility
  802.15.4a conflates time-of-flight ranging and data transmission

## Slide 18: Harmonium: Decouple ranging and data to realize low-power, high-speed, high-fidelity tracking
Harmonia: Wideband Spreading for Accurate Indoor RF Localization (HotWireless’14)
Harmonium: Asymmetric, Bandstitched UWB for Fast, Accurate, and Robust Indoor Localization (IPSN’16)
Benjamin Kempke, Pat Pannuto, and Prabal Dutta
Tag weighs 3g and costs ~$4.50
Draws 75mW transmitting, 3.9mJ / fix
14cm median 31cm 90%ile
Key tradeoff is asymmetry

## Slide 19: Insight: The harmonics of a sharp pulse are a UWB signal (thus, “Harmonium”)
Concept of operation:
  BJT NPN Pulse generator
  Monoflop generator
  Pulse Repetition Frequency (PRF) generator
  Trigger filter
  Pulse-shaping filter
5 GHz
6 GHz

## Slide 20: Pulse train generation
Notes: Notes: Uses ASE-4.000MHZ-LC-T (+/- 50 ppm)

## Slide 21: Pulse train generation

## Slide 22: Pulse train generation

## Slide 23: Pulse train generation

## Slide 24: Pulse train generates a UWB signal
Pulse w/o filtering

## Slide 25: Nit: filter input trigger
Pulse w/o filtering  Pulse w/ trigger filtering

## Slide 26: UWB spectral mask starts at 3.1 GHz
Pulse w/o filtering  Pulse w/ trigger filtering

## Slide 27: The Harmonium signal for $4.50 and 75 mW
Pulse w/o filtering  Pulse w/ trigger filtering  Pulse w/ shaping filter

## Slide 28: Measure the time-difference-of-arrival to estimate the location of the tag
Anchor-global, synchronized clock
Commercial UWB receivers expect standard packets and modulation

## Slide 29: Harmonium: UWB Reception with Narrowband Radios
Concept of operation:
  Generic narrowband receiver
  Frequency-swept local oscillator
  Antenna diversity

## Slide 30: Harmonium: UWB Reception with Narrowband Radios
Concept of operation:
  Generic narrowband receiver
  Frequency-swept local oscillator
  Antenna diversity

## Slide 31: Harmonium: UWB Reception with Narrowband Radios
Concept of operation:
  Generic narrowband receiver
  Frequency-swept local oscillator
  Antenna diversity

## Slide 32: Harmonium: UWB Reception with Narrowband Radios
Concept of operation:
  Generic narrowband receiver
  Frequency-swept local oscillator
  Antenna diversity

## Slide 33: Harmonium: UWB Reception with Narrowband Radios
Concept of operation:
  Generic narrowband receiver
  Frequency-swept local oscillator
  Antenna diversity

## Slide 34: Harmonium reconstructing UWB signals in the real world

## Slide 35: Time-of-arrival estimation from a real-world trace

## Slide 36: Harmonium successfully tracks micro quad-rotors accurately and with minimal impact
14 cm median error
46 cm 95%ile error
Up to 1.4 m/s
19 Hz sampling

## Slide 37: SurePoint lasts at best a few hours, Harmonium a few days – can we do better?
How might an energy-harvesting localization system work?

## Slide 38: Slocalization: Backscatter-based UWB localization
Energy-harvesting tag drives PN code through a shift register loading/unloading an antenna
Well below noise floor, but integration in a static environment can reveal the tag signal
Longer PN code  more tags & slower localization

## Slide 39: We are only beginning to scratch the surface of the UWB localization space
SurePoint
  Robust, reliable, with excellent long-tail performance
Harmonium
  Lower tag energy, area, and cost but anchor sync hinders deployment
Slocalization
  Vastly lowest energy, but update rates in the minutes / fix
Other opportunities…
  Solve for anchor positions, no measuring?
  SurePoint tags range in parallel, eavesdropping?
  UWB CIR underutilized?

## Slide 40: For More Information…
http://github.com/lab11
  lab11/fast-square [harmonium]
  lab11/polypoint [SurePoint]
http://patpannuto.com
Notes: Our lab website is down. Lame 

## Slide 41: Luxapose: Astral navigation with smart phones and smart lights
Luxapose: Indoor Positioning with Mobile Phones and Visible Light (MobiCom’14)
Ye-Sheng Kuo, Pat Pannuto, Ko-Jen Hsiao, and Prabal Dutta

## Slide 42: Luxapose enables high-fidelity indoor localization with impending infrastructure
Luxapose: Indoor Positioning with Mobile Phones and Visible Light (MobiCom’14)
Ye-Sheng Kuo, Pat Pannuto, Ko-Jen Hsiao, and Prabal Dutta
Human Perception
Camera Perception
Decimeter-level accuracy
Unmodified smartphones
Trivially modified LED lights

## Slide 43: Opo: Forgoing absolute location for high fidelity relative location
Application
  Human Interaction Tracking
Key Tradeoffs
  Ranging Accuracy
  Duration Accuracy
  Usability
Opo
  5 cm accuracy, 2 s minimum interaction, 93 hour battery life
Opo: A Wearable Sensor for Capturing High-Fidelity Face-to-Face Interactions (SenSys ‘14)
William Huang, Ye-Sheng Kuo, Pat Pannuto, and Prabal Dutta

## Slide 44: Localization research needs to solve systems problems
Time
Accuracy (m)
10.00
1.00
0.01
0.10
WASP [‘11/0.50]
2008
2011
2014
2017
Harmonia [‘14/0.40], RF-IDraw [‘14/0.38]
Tagoram [‘14/0.12], WiTrack [‘14/0.12]
PolyPoint [‘15/0.31]
Harmonium [‘16/0.09]
WREN [‘13/2.00]
3D-LOCUS [‘09/<0.01]
Salathé [‘10/2.00]
Social fMRI [‘11/5.00]
Opo [‘14/0.05]
SurePoint [‘16/0.29]
If you believe in the IoT/IoE
  100’s, 1000’s in one room?
Ground truth for anchors?
  Anchors at all?
Localization technology as a privacy policy
  SurePoint vs. Harmonium
  vs. ALPS vs. Luxapose

## Slide 45: Location technology maturing and will become commonplace
Today’s digital things have a few fundamental primitives
  “Sense of Self”
  “Sense of Time”
Tomorrow’s things will include a “Sense of where”
The long tail is full of interesting research
  There are devices for whom a sense of time is difficult today
  There will be those for whom location is difficult tomorrow
  Drives novel systems and technological solutions