## Slide 1: The Recent Past and Distant Future of [Micro-Scale] Embedded Systems
Pat Pannuto, University of Michigan
ppannuto@umich.edu, patpannuto.com
NextMote Workshop @ EWSN’16, Graz, Austria
February 15, 2016

## Slide 2: “Micro-Scale” are systems whose principle node dimension is measured on the order of millimeters
Today’s motes are decimeter-scale…
…and pushing towards centimeter-scale

## Slide 3: A millimeter-sized system is a 1000x reduction in volume
In practice, several nodes fit on a period.

## Slide 4: We have developed dozens of millimeter-scale motes as part of the Michigan Micro Mote (M3) project

## Slide 5: This talk: A tour of micro-scale mote challenges
A Brief History of “Smart Dust”
Micro-Scale Composition Architecture
Energy
Communication
Debugging

## Slide 6: This talk: A tour of micro-scale mote challenges
A Brief History of “Smart Dust”
Micro-Scale Composition Architecture
Energy
Communication
Debugging

## Slide 7: “Smart Dust” is not new…
1957: Fred Hoyle’s Black Cloud
  Sentient space-faring cloud organism
Early-mid 90’s: Viable?
  First serious discussions at RAND and ISAT workshops
1995: Neal Stephenson’s Diamond Age
  Popularized a modern vision of smart dust
1998: Kris Pister coins the term
  And starts making smart dust a reality!

## Slide 8: First-generation smart dust missed its 1mm3 goal, but their so-called “macro motes” were perhaps the most important
Ad-hoc composition lessened efficiency of volumetric space
Early “macro motes” dovetailed and helped drive early “mote” development
1999
900 MHz radio
Magnetometer
Accelerometer
Light
Temperature
Pressure
One week lifetime in continuous operation,
2 years w/ 1% duty cycle
http://robotics.eecs.berkeley.edu/~pister/SmartDust/

## Slide 9: The history of modern mote research picks up around this time
Pister & Hollar’s
“Macro Motes”
CSP Workshop @ Xerox PARC
[soon to be IPSN]
Workshop on Wireless Sensor Networks and Applications
[soon to be SenSys]
First MICA
BTNode
Great Duck Island
TelosB
(Tmote Sky)
Epic Core
(modular
platforms)
B-MAC
Glossy
Notes: Collaborative Signal Processing Workshop (CSP Workshop)

## Slide 10: But what happened to research pushing towards a 1mm3 system?
?

## Slide 11: We stopped building mm-scale systems, and focused on mm-scale circuits – at least for a little while
Y.-S. Lin ‘08
V. Ekanayake ‘04
B. Warneke ‘04
M. Scott ‘03
Y.-S. Lin ‘07
2008 The Phoenix Project

## Slide 12: Monolithic designs let us push the envelope, but modularity must return to grow beyond a niche space
Phoenix
  World’s lowest power computer (30 pW / 300 nW)
  Basically a temperature sensor
Intraocular Pressure
  Collaboration for glaucoma health
  A pressure sensor
The Phoenix Processor: A 30pW Platform for Sensor Applications, Mingoo Seok, Scott Hanson, Yu-Shiang Lin, Zhiyoong Foo, Daeyeon Kim, Yoonmyung Lee, Nurrachman Liu, Dennis Sylvester, David Blaauw , VLSI ‘08
A Cubic-Millimeter Energy-Autonomous Wireless Intraocular Pressure Monitor, Gregory Chen, Hassan Ghaed, Razi-ul Haque, Michael Wieckowski, Yejoong Kim, Gyouho Kim, David Fick, Daeyeon Kim, Mingoo Seok, Kensall Wise, David Blaauw, Dennis Sylvester, ISSCC ‘11
2008
2011
From mm-scale temperature sensor to mm-scale pressure sensor took 3 years
(and another half-dozen PhD students…)

## Slide 13: Today, we are able to mix and match components to synthesize systems
2 uAh Battery
5 uAh Battery
Decap
Control/
PMU
Temp Sensor
Radio
+ CDC
Motion Detection/ Imager
Pressure Sensing
Temp. Sensing
MEMS
P. Sensor
Visual Sensing

## Slide 14: However, we had to invent a new system interconnect to be able to do it
2 uAh Battery
5 uAh Battery
Decap
Control/
PMU
Temp Sensor
Radio
+ CDC
Motion Detection/ Imager
Pressure Sensing
Temp. Sensing
MEMS
P. Sensor
Visual Sensing

## Slide 15
A Brief History of “Smart Dust”
Micro-Scale Composition Architecture
Energy
Communication
Debugging

## Slide 16: Comparing system composition strategies between traditional motes and mm-scale motes
How to build a mote to sense temperature today?
  Processor
  Temperature Sensor
  Radio
How to build a mm-scale mote to sense temperature?
  temp_sense t1 (
    …
    .sample_valid_out (to_proc_t1_sample_valid),
    .sample_out (to_proc_t1_sample),
    );
  processor p1 (
    …
    .temp_valid_in (to_proc_t1_sample_valid),
    .temp_in (to_proc_t1_sample),
    );

## Slide 17: We have solutions for composing embedded systems… SPI and I2C
Nearly every microcontroller has both
Nearly every peripheral has one or the other
Very few use anything else
  (except maybe UART)
So why don’t they work for mm-scale systems?

## Slide 18: Millimeter-scale systems are small
Budget 10’s μW active, 10’s nW sleep, DC 0.1%
Node volume is dominated by energy storage
And volume is shrinking cubically
Battery
“Phone”
Batteries
“Sensor”
Battery
“Sensor”

## Slide 19: Millimeter-scale systems are small
Node volume is dominated by energy storage
And volume is shrinking cubically
I/O pads begin to account for non-trivial percentage of node surface area
Battery
“Phone”
Batteries
“Sensor”
Battery
“Sensor”
1 mm = 1,000 μm
50 μm, minimum viable bond pad
16-20 maximum I/O pins for 3D stacking
Budget 10’s μW active, 10’s nW sleep, DC 0.1%

## Slide 20: What is wrong with how are systems composed today?
SPI, invented by Motorola in ~1979
One master, N slaves
Shared clock: SCLK
Shared data bus: MOSI
Shared data bus: MISO
One Slave Select line per slave
Key Properties
    One dedicated I/O line per slave
  Master controls all communication
SCLK
MOSI
MISO
SS
Slave 1
SCLK
MOSI
MISO
SS
Slave 2
SCLK
MOSI
MISO
SS0
SS1
…
Master
Notes: Extremely populare; almost all MCUs have this interface

## Slide 21: What is wrong with how are systems composed today?
One master, N slaves
Shared clock: SCLK
Shared data bus: MOSI
Shared data bus: MISO
One Slave Select line per slave
One interrupt line per slave
Key Properties
    One Two dedicated I/O lines per slave
  Master controls all communication
    Interrupts must be out-of-band
SCLK
MOSI
MISO
SS
INT
Slave 1
SCLK
MOSI
MISO
SS
INT
Slave 2
SCLK
MOSI
MISO
SS0
SS1
…
GPIO0
GPIO1
…
Master
SPI, invented by Motorola in ~1979

## Slide 22: SPI’s I/O overhead and centralized architecture do not scale to mm-scale systems
One master, N slaves
Shared clock: SCLK
Shared data bus: MOSI
Shared data bus: MISO
One Slave Select line per slave
One interrupt line per slave
Key Properties
    One Two dedicated I/O lines per slave
  Master controls all communication
    Interrupts must be out-of-band
SCLK
MOSI
MISO
SS
INT
Slave 1
SCLK
MOSI
MISO
SS
INT
Slave 2
SCLK
MOSI
MISO
SS0
SS1
…
GPIO0
GPIO1
…
Master
SPI, invented by Motorola in ~1979

## Slide 23: SPI’s I/O overhead and centralized architecture do not scale to mm-scale systems
SCLK
MOSI
MISO
SS
INT
Slave 1
SCLK
MOSI
MISO
SS
INT
Slave 2
SCLK
MOSI
MISO
SS0
SS1
…
GPIO0
GPIO1
…
Master
SPI, invented by Motorola in ~1979
1 mm = 1,000 μm
50 μm, minimum viable bond pad
16-20 maximum I/O pins for 3D stacking

## Slide 24: I2C has fixed I/O requirements and a decentralized architecture
I2C, invented by Phillips in 1982
  Any-to-(m)any on one shared bus
Key Properties
  Fixed wire count (2)
SCL
SDA
Node1
SCL
SDA
Node3
SCL
SDA
Node2

## Slide 25: I2C has fixed I/O requirements and a decentralized architecture
I2C, invented by Phillips in 1982
  Any-to-(m)any on one shared bus
Key Properties
  Fixed wire count (2)
  Open-collector
    Multi-master
    Flow Control
SCL
SDA
Node1
SCL
SDA
Node3
SCL
SDA
Node2
Open-collector (aka wired-AND)

## Slide 26: The problem is the energy costs of running an open-collector
Send a “1”: 0 J
VDD = 1.2 V
Send a “0”: 174 pJ
@400 kHz
80% VDD as 1
R = 15.5 kΩ
(“the best”)
No setup, no hold

## Slide 27: The problem is the energy costs of running an open-collector
Send a “1”: 0 J
VDD = 1.2 V
R = 15.5 kΩ
(“the best”)
Send a “0”: 174 pJ
SCL Alone: 70 μW
@400 kHz
80% VDD as 1
@400 kHz
No setup, no hold
Bigger R?

## Slide 28: The problem is the energy costs of running an open-collector
Send a “1”: 0 J
VDD = 1.2 V
Send a “0”: 174 pJ
SCL Alone: 70 μW
@400 kHz
80% VDD as 1
@400 kHz
~ 3.1 mm
Two batteries
Active Energy Budget: 20 μW
Not an arbitrary number:
  Volume Target
  Lifetime Target
R = 15.5 kΩ
(“the best”)
No setup, no hold

## Slide 29: The energy demands of open-collectors make them unsuitable for mm-scale systems
SCL Alone: 70 μW
~ 3.1 mm
Two batteries
Active Energy Budget: 20 μW
Not an arbitrary number:
  Volume Target
  Lifetime Target
@400 kHz
@400 kHz
Notes: Design for 20, try to hit 40 in practice

## Slide 30: The design and synthesis of modular, millimeter-scale systems requires a new embedded interconnect

## Slide 31: MBus is a clean-slate design, built to satisfy interconnect requirements for this and the next generation of motes
Fixed pin count (4)
Minimal standby and active power
Large global address space
Multi-master design
Broadcast message support
Hardware acknowledgements
Data independent behavior
Modest protocol overhead
Power aware design
MBus: An Ultra-Low Power Interconnect Bus for Next Generation Nanopower Systems
Pat Pannuto, Yoonmyung Lee, Ye-Sheng Kuo, ZhiYoong Foo, Benjamin Kempke, Gyouho Kim, Ronald G Dreslinski, David Blaauw, and Prabal Dutta
Proceedings of the 42nd International Symposium on Computer Architecture (ISCA ’15)

## Slide 32: MBus in a nutshell
MBus Mediator
MBus Member
MBus Member
MBus Member
MBus Member
Clock
Data
Ring Topology
2 lines – 4 I/O per node
  Clock
  Data
Transaction oriented
  Arbitration
  Address Transmission
  Data Transmission
  Interjection
  Control (ACK/NAK)
“Shoot-Through”
CLK_IN
CLK_OUT

## Slide 33: Embedded interconnect technology has not changed in over 30 years
If we re-examine…

## Slide 34: Embedded interconnect technology has not changed in over 30 years
If we re-examine…
  Addressing
Requires I/O not available
Makes packaging assumptions
  Systems will not always be PCBs
  Routing may not be easy
    3D stack
    Flip-chip + TSVs

## Slide 35: Embedded interconnect technology has not changed in over 30 years
If we re-examine…
  Addressing
3 Options
  Short static addresses and allow device conflicts
  Long static addresses to avoid device conflicts
  Non-static addresses
MBus does all 3
  4-bit: Static short prefixes (device class)
  24-bit: Static long prefixes (unique device ID)
  4-bit: Runtime enumeration protocol (replaces short prefix)

## Slide 36: Embedded interconnect technology has not changed in over 30 years
If we re-examine…
  Addressing
  Acknowledgements
I2C acknowledges every byte
  How often do NAKs happen?
    To a random byte?
  12.5% overhead
MBus ACKs transactions
  Receiver can interject message

## Slide 37: Embedded interconnect technology has not changed in over 30 years
If we re-examine…
  Addressing
  Acknowledgements
  Centralized vs Decentralized
Sensor
CPU
Radio
Over 2x energy consumption with centralized
7% improvement in lifetime for a prototypical “sense & send” application
Sensor
Radio
CPU

## Slide 38: Existing interconnect technology cannot service forthcoming motes, and may be hindering current motes
Leading embedded interconnects are showing flaws
  Unbounded I/O requirements
  Burdensome runtime energy demands
  Limited addressing schemes
  Inefficient or nonexistent acknowledgments
  Restrictive centralized architecture
MBus addresses all of these issues and adds new features

## Slide 39: Energy is a looming system synthesis problem
A Brief History of “Smart Dust”
Micro-Scale Composition Architecture
Energy
Communication
Debugging

## Slide 40: Motes embraced “dark silicon” first
Powering off regions of a chip has become commonplace
Motes power off regions of a system
  Requires coordination strategy
  Historically the CPU
  Putting peripherals into
  standby mode was good
  enough for early, battery-
  backed motes…
1999
900 MHz radio
Magnetometer
Accelerometer
Light
Temperature
Pressure
One week lifetime in continuous operation,
2 years w/ 1% duty cycle

## Slide 41: Energy-critical systems push from “dark silicon” to “pitch black” silicon
Clock-gating
  Stop driving the clock tree of regions of a chip
  Eliminates switching power, but not static leakage
  “Dark Silicon”
Power-gating
  Switch off power to regions of a chip
  Eliminates all chip leakage
  “Pitch Black Silicon”
M3 systems aggressively power-gate to reach energy budget

## Slide 42: Energy-harvesting motes embrace “pitch black” silicon Can we build a (useful) battery-free mote? Mote platform?
L. Yerva, B. Campbell, A. Bansal, T. Schmid, and P. Dutta, “Grafting Energy-Harvesting Leaves onto the Sensornet Tree,” In Proceedings of the 11th International Conference on Information Processing in Sensor Networks (IPSN'12), Beijing, China, Apr. 16-20, 2012.
“The Nuclear Option”
Zero static leakage
Very little control
Slide borrowed from Prabal Dutta

## Slide 43: Monjolo sensors—the harvester is the sensor
Monjolo: A Portuguese water hammer
Hammer rate  flow rate
Fixed water quanta / strike
Non-linearity with high flow rate
L. Yerva, B. Campbell, A. Bansal, T. Schmid, and P. Dutta, “Grafting Energy-Harvesting Leaves onto the Sensornet Tree,” In Proceedings of the 11th International Conference on Information Processing in Sensor Networks (IPSN'12), Beijing, China, Apr. 16-20, 2012.
B. Campbell, B. Ghena, and P. Dutta, "Energy-Harvesting Thermoelectric Sensing for Unobtrusive Water and Appliance Metering,” In Proceedings of the 2nd International Workshop on Energy Neutral Sensing Systems (ENSsys'14), Memphis, TN, Nov. 6, 2014.
Samuel DeBruin, Bradford Campbell, and Prabal Dutta, "Monjolo: An Energy-Harvesting Energy Meter Architecture,” In Proceedings of the 11th ACM Conference on Embedded Networked Sensor Systems (Sensys'13), Rome, Italy, Nov. 11-14, 2013.
Slide borrowed from Prabal Dutta

## Slide 44: The Monjolo principle decomposes into an array of components that build a diverse set of energy-harvesting sensors
HW/SW designs available online:
[1] http://lab11.eecs.umich.edu/pcb.html
[2] https://github.com/lab11
Slide borrowed from Prabal Dutta

## Slide 45: Systems are not required to be all or none, however
“Federated Energy”
  Harvest an independent store for each component
  Completely cut power when component is not in use
  But this system cannot cut power to the MCU
  MCU-Federated energy control
Josiah Hester, Lanny Sitanayah, and Jacob Sorber. 2015. Tragedy of the Coulombs: Federating Energy Storage for Tiny, Intermittently-Powered Sensors. In Proceedings of the 13th ACM Conference on Embedded Networked Sensor Systems (SenSys '15)

## Slide 46: Embedded interconnect technology has not changed in over 30 years
If we re-examine…
  Addressing
  Acknowledgements
  Centralized vs Decentralized
  Peripheral power state is an interconnect concern

## Slide 47: Our mm-scale systems leverage decentralized, autonomous power management via MBus
Key Challenges
  Energy efficient multi-master systems are a distributed state problem
  Cold-booting silicon is a hard circuits problem
    Because there is no stable clock
MBus Key Observation
  A component is either already on, or can leverage an incoming message to wake itself

## Slide 48: MBus introduces three, transparent, hierarchical power domains to maximize efficiency
Provide an “always-on” abstraction
  Interconnect fabric powers on components upon receipt of a message
  Transparent to callers and chip designers

## Slide 49: As motes continue to push the boundaries of lifetime, harvesting, and volume, every microjoule is precious
Circuits advancements will continue to provide benefits
  Non-volatile RAM will fall in price and area
  Accelerators will replace compute-intensive tasks
  Finer-grained internal power-gating
  Diminishing returns…
But there are system-level constructs wasting energy today
  Leveraging peripheral power-gating
  Coalescing wakeups
  Clock domain controls
  …

## Slide 50
A Brief History of “Smart Dust”
System Composition Architecture
Energy
Communication
  “Internal”
  “External”
Debugging

## Slide 51: Embedded interconnect protocols have not changed in 30 years either
In fact, they do not exist at all
Q: How do you read a register on a sensor?
Q: How do you write to a radio’s packet buffer?

## Slide 52: MPQ: A (mostly) PHY-independent protocol to standardize reading and writing registers and memory
Motivations
  Simplicity across the ecosystem
  Enabling reliable direct peripheral communication
  Transition CPU from active overseer to passive coordinator
    Configure all peripherals at boot, then power off self
    Distributed equivalent of many COTS chips (Sleepwalking, uDMA, etc)
Primitives
Read/Write Register
Block DMA transfer
“Streaming” memory

## Slide 53: MPQ repurposes the 4 LSB of the address as a function identifier
  Could also use the first 4 bits of data if address bits are unavailable
  Embedded write addresses for read commands enable powerful command synthesis

## Slide 54: An interesting quirk begets an interesting question
M3 CPU chip has only SRAM
  Loses state (and programming) on complete power loss
Separate flash chip programs CPU on boot
  Actually, it is a state machine issuing arbitrary DMA messages
No CPU needed for a sense, send, and forget application
  As peripherals become more capable, what is the role of the CPU?

## Slide 55: Perhaps it is time for a generic protocol on top of major embedded buses
Improve the programmability and utility of mostly-fixed-function peripheral frontend
Proving powerful for synthesis in M3 ecosystem
Easy to phase-in
  No backward compatibility because there’s nothing today!

## Slide 56
A Brief History of “Smart Dust”
System Composition Architecture
Energy
Communication
  “Internal”
  “External”
Debugging

## Slide 57: Q: How do you program a 1mm3 mote?
Actual size

## Slide 58: A 695 pW, always-on visible light communication receiver

## Slide 59: A sub-nanowatt receiver opens interesting possibilities for traditional motes
Idle listening dominates energy budget of many MACs
Can we decouple synchronization from communication?
Real time
Local time
Staying Synchronized
300 s
Guard
1200 μs
@ 2ppm
Static Power:
~100 nW

## Slide 60: All this begs the question, what else can we do with an intelligent lighting infrastructure?
System Architecture Directions for a Software-Defined Lighting Infrastructure
Ye-Sheng Kuo, Pat Pannuto, and Prabal Dutta
1st ACM Workshop on Visible Light Communication Systems (VLCS ’14)

## Slide 61: The capabilities of VLC receivers vary greatly
Diffusing (single photodiode)
Simpler devices
   Less computation capability
Cannot distinguish transmitters
Requires temporal signal diversity
Array (multiple photocell)
Can distinguish transmitters
Temporal or spatial diversity

## Slide 62: Luxapose: Astral navigation with smart phones and smart lights
Luxapose: Indoor Positioning with Mobile Phones and Visible Light (MobiCom’14)
Ye-Sheng Kuo, Pat Pannuto, Ko-Jen Hsiao, and Prabal Dutta

## Slide 63: Luxapose enables high-fidelity indoor localization with impending infrastructure
Luxapose: Indoor Positioning with Mobile Phones and Visible Light (MobiCom’14)
Ye-Sheng Kuo, Pat Pannuto, Ko-Jen Hsiao, and Prabal Dutta
Human Perception
Camera Perception
Decimeter-level accuracy
Unmodified smartphones
Trivially modified LED lights

## Slide 64: Can smart dust and smart phones co-exist on the same lighting infrastructure?

## Slide 65: With sufficient synchronization, transmitted signals can constructively interfere

## Slide 66: Emerging non-traditional (non-narrowband RF) communication technologies are just beginning exploration
Sub-nanowatt VLC receivers
VLC retroreflectors for bi-directional communication
Acoustic?
Vibratory?
Backscatter communication
High-fidelity localization with UWB
  For almost no power with backscattered UWB?

## Slide 67
A Brief History of “Smart Dust”
System Composition Architecture
Energy
Communication
Debugging

## Slide 68: An open question: How to effectively debug a system you cannot touch?
Debug chips provide some introspection
  Snoop (or inject) on system bus
  Power traces remarkably effective
Encapsulated systems remain a big issue
Bottom View: MEMS pressure sensor
Side View: Light-blocking epoxy
Top View: Clear epoxy for harvesting

## Slide 69: Many further questions in this space for future motes
When is an energy harvesting node dead or just harvesting?
How to debug 1,000 nodes?
  How to find “the” bad node among 1,000?
  How to collect and recover failed nodes?
    Or is it really just dust? 

## Slide 70: Everyone’s favorite debugging answer: Write something well enough that it won’t crash!
A teaser for Tock
  New embedded operating system
    Collaboration with Stanford and UC Berkeley
  Defense-in-depth: language (Rust) and hardware (MPU) protections
  It’s time for proper kernel/application separation
    Even viable for micro-scale processor (currently M0, but M0+ has MPU)
And a safe, accessible user-space runtime (Lua)

## Slide 71: What have we learned from the development of millimeter-scale systems?
Existing system synthesis technologies cannot scale
Revisiting long-standing architectural components can yield unforeseen benefits
To maximize energy efficiency, power-awareness must permeate every aspect of the system design
New communication technologies are setting up major architectural shifts
There is lots of work yet to do!

## Slide 72: http://mbus.io http://github.com/mbus http://lab11.eecs.umich.edu http://github.com/lab11
Pat Pannuto, University of Michigan
ppannuto@umich.edu, patpannuto.com

## Slide 73: Gartner Hype Cycle
Appeared 2013, fell off 2014, back in 2015
[2013]: http://www.gartner.com/newsroom/id/2575515
[2014]: http://www.gartner.com/newsroom/id/2819918
[2015]: http://www.gartner.com/newsroom/id/3114217