## Slide 1: Sensor Systems and the Art of Effectively Deploying Sensor Networks
Pat Pannuto
University of Michigan
TechChange – TC111

## Slide 2: CellPump: Using sensors to improve efficacy
30-80% of water pumps fail within 1 year of installation
What happens when a pump fails?
http://www.pdx.edu/sweetlab/cellpump-rwanda
http://www.sweetsensors.com/applications/cellpump/

## Slide 3: Stove Usage Monitors: Establishing reliable usage data
How much are free cookstoves actually used?
https://www.youtube.com/v/qmY8PRmi3lQ

## Slide 4: Inspire Living: Sensors for Immediate Impact
Pneumonia can be reliably diagnosed from key signals
  Respiration rate is key
Hard to train people to diagnose, easy to train a machine
  Use sensors to measure and evaluate respiration

## Slide 5: Application requirements define data behavior
CellPump Stove Usage Monitors Inspire Living
Real-Time Batch Local Loop
Has Pneumonia
Consult Doctor

## Slide 6: Developing a sensor-based deployment requires understanding…
What semantic data you need?
  What is the question you’re actually trying to answer?
What physical data you need?
  What can you actually sense about the world?
What do you have available?
  Existing data sources, infrastructure
How is the data intended to be used?
  Which informs how the data is collected, disseminated
A sensor deployment is a series of interconnected tradeoffs
Notes: Semantic: Is the water pump working? Stretch: how much is it being used? Physical: Water flow meter (expensive, fluids are hard). Handle motion (easy to measure, hard to conceal). Vibrations inside the pump?  requires experimentation
Resources: Synergistic data sources
Use: Real-time vs. batch. Personal data / protection? Feedback to users (and the ramifications of lifestyle adjustment due to your tech)

## Slide 7: Sometimes semantic and physical data requirements line up
How does interior temperature change through the day?
  Use a temperature sensor
What about humidity, carbon dioxide, air particulates…?
  In general, there are sensors for environmental monitoring

## Slide 8: Many times we have to look at side effects to sense phenomenon
Simple Example
Did I close the window  Contact sensor
Did I close the blinds  Ambient light sensor
Complex Example
Fitbit “counts steps”
Measures accelerometer data
Classifies motion traces
(machine learning usually)

## Slide 9: Choosing a means to sense can be non-obvious
“I need a sensor that measures water flow”
  Mechanically challenging
“It needs to be wireless and last for several months”
“I want to measure if people wash their hands after they use the toilet”
You actually want a temperature sensor
Paul Martin, Zainul Charbiwala, Mani B. Srivastava
DoubleDip: leveraging thermoelectric harvesting for low power monitoring of sporadic water use
In Sensys’10

## Slide 10: Group Question: How can we answer the same question without plumbing?
Goal: Measure hand washing rate after bathroom usage
Stretch goal: Distinguish by bathroom activity
Restrictions:
No plumbing
No power
No direct user involvement (“push here after washing”)

## Slide 11: What data sources are already available?
Sometimes what you want is collected and published
  KPLC weekly power outage reports
Use partial information to confirm or question measurements
Notes: KPLC has problems – trust the utility? PDF document of data hard to use. Coarse-granularity

## Slide 12: Think a little outside the box for possible data sources
Kenya: people tweet to notify / complain of power outages
Preliminary results from a deployment in Kenya

## Slide 13: Drilling into data collection and tradeoffs
What semantic data you need?
  What is the question you’re actually trying to answer?
What physical data you need?
  What can you actually sense about the world?
What do you have available?
  Existing data sources, infrastructure
How is the data intended to be used?
  Which informs how the data is collected, disseminated
A sensor deployment is a series of interconnected tradeoffs
Notes: Semantic: Is the water pump working? Stretch: how much is it being used? Physical: Water flow meter (expensive, fluids are hard). Handle motion (easy to measure, hard to conceal). Vibrations inside the pump?  requires experimentation
Resources: Synergistic data sources
Use: Real-time vs. batch. Personal data / protection? Feedback to users (and the ramifications of lifestyle adjustment due to your tech)

## Slide 14: Define the data you intend to collect
How much data?
  Synchrophasor (power grid health): 1000’s samples / sec
  Soil Moisture: 1-10 samples / day
  Mudslide Detection1: 1 sample / 5 min <> 10 samples / sec
And what data do you actually need?
  12:00 AM – It’s 74 degrees.
  12:01 AM – It’s 74 degrees.
  12:02 AM – It’s 74 degrees.
  “Compressive sensing”
    Lots of research: Report differences, trends, fit variables…
1Real-time Wireless Sensor Network for Landslide Detection. Ramesh, M. V. SenSys’13

## Slide 15: Energy budget defines capabilities (and requirements dictate energy budget)
Plug it in!
  Power grid can be unreliable
  Requires nearby available wiring
  Who pays?
Put a battery in it
  Battery == Lifetime
  Low-power design or a big battery
What about solar?
  Energy harvesting often most expensive
  Requires lowest-power design

## Slide 16: The cost / performance tradeoff spans 2-3 orders of magnitude
“An embedded sensor is like a computer from
the ’70s with some neat sensors attached”
and lasts a year+ on a battery
“A smartphone is like a mini-PC in your pocket”
and lasts a day on a battery

## Slide 17: The cost / performance tradeoff spans 2-3 orders of magnitude
“An embedded sensor is like a computer from
the ’70s with some neat sensors attached”
“A smartphone is like a mini-PC in your pocket”
They are priced appropriately

## Slide 18: Smartphones have a diverse array of powerful sensors
Smartphones have a diverse array of powerful sensors
Accelerometer, Gyroscope, Magnetometer, GPS, camera…
And communication (cellular, WiFi, Bluetooth, NFC) is built in
Pentland ‘09
Pentland ‘06
Pentland ‘07

## Slide 19: HiJack: Augmenting smartphones to add “missing” sensors
Geiger Counter
CO Sensor
CC Terminal
EKG Monitor
Thermometer
Soil Moisture
[slide courtesy Prabal Dutta]

## Slide 20: HiJack  QuickJack  PhoneWorks
Commercial development kit available, mass market products
Images from NXP, Home Depot

## Slide 21: Smartphones are expensive to deploy
General purpose device: you pay for what you don’t use
Power limitations means the phone is tethered
  Unless “attached” to a user, that is, crowdsourcing
Communication options only cellular, Wi-Fi, Bluetooth
Make sense in 10s-100s, maybe not 1000s
  But can be re-used / re-purposed

## Slide 22: How to think like an embedded systems engineer
Or, how to do better than a smartphone for less money?
Goal: Understand the tradeoffs in the embedded design space, what is feasible, what isn’t feasible.

## Slide 23: How much local storage do you need?
It’s never zero
  How much data are you willing to lose?
  “Batch”, “Delay-Tolerant”, “Best-Effort”
Memory quickly drives microcontroller cost
  RAM from 16~128 kilobytes
Flash memory
  SD cards are cheap, easy to interface with
  Flash chips can be cheaper, more work to integrate; read
What do you do when you run out of space?

## Slide 24: How do you get continuous data off of devices?
What data backhaul is available?
  Ethernet? Wi-Fi? Cellular (data, voice, text)? Satellite?
  How reliable is it?
    (again, how much data are you willing to lose?)
Who Pays??
Communication is often 80%+ of energy budget
  Defines battery size / system lifetime
Notes: Who pays – buy SIMs? Pay users per report? How to share internet uplink? App-based BW-metering is really hard. Satellite is really expensive.

## Slide 25: Is there anything that can make communication more efficient?
Costs less energy to send a smaller distance (usually)
  e.g. Wi-Fi uses less energy than cellular
Mesh Networks
  Popular in wireless sensor network research
    Hard to make reliable in practice for battery-backed devices
  iOS 7 adds support for Wi-Fi based mesh networking
    Not used much yet, something to watch
    Early reports are many of the same difficulties as WSNs

## Slide 26: Taking it to the extreme: Full-custom design of a $25 “radio DVR”
FM receiver that records broadcast lessons
Users can record programs and share them
http://www.bbc.com/news/technology-30127578
http://web.eecs.umich.edu/~prabal/pubs/papers/foo13lit.pdf

## Slide 27: Taking it to the extreme: Full-custom design of a $25 “radio DVR”
http://www.bbc.com/news/technology-30127578
http://web.eecs.umich.edu/~prabal/pubs/papers/foo13lit.pdf

## Slide 28: Wireless sensor networks are young technology
The field is 15-20 years old
Maker culture creating some accessible technology
Notes: “arduino battery life”: https://hwstartup.wordpress.com/2013/03/11/how-to-run-an-arduino-on-a-9v-battery-for-weeks-or-months/
Tessel consumes about 1 Watt when it has the CC3000 WiFi radio enabled and is running blinky.js.
Pinnocio – 27 hours full bore; claims duty cycling. Radio = 17 mA.

## Slide 29: GridWatch: Crowdsourcing power grid health monitoring
Insight: You pick up your phone to unplug it
  Power loss without motion is likely a power outage
[GridWatch HotMobile ‘14]

## Slide 30: Smoking Cessation with Monoxalyze
Smoking Cessation programs lack feedback
  Q: Did you smoke today?
  A: No, of course not!
Carbon Monoxide levels reveal smoking within 4-6 hours
Gen 2: Wireless (BLE), Authenticated

## Slide 31: Human interaction tracking and social graph building with Opo
1.6 cm
Wearable
Detailed
Accurate
Small form factor
Ranging Accuracy Test
Two Person Interaction
A Week as a PhD Student
Fine-grained human interaction data
  Who did you talk to today?
  For how long?
  10 cm accuracy with 1 week battery
Applications in sociology, immunology

## Slide 32: Wearabouts: Leveraging wearable electronics for building occupancy
Wearables are everywhere….
Most emit beacons we can listen for
Which we use to locate people in space

## Slide 33: The Monjolo Principle Combining non-traditional sensing and energy harvesting
Harvest side-channels of energy – wakeup frequency is the sensor
[Monjolo, Sensys ‘13]

## Slide 34: Takeaways
Anything can be sensed, but it may require creativity
Distinguish what you want to know from what you need to measure to answer the question
Constraints on data-collection define the rest of your system
Or at the least are a very good place to start
Smartphones are useful, but not a panacea
And can be costly (though re- and multi-purposeable)

## Slide 35: Contact and More Information
Pat Pannuto
pat.pannuto@gmail.com
http://patpannuto.com
[slides on my website]
Lab11
http://lab11.eecs.umich.edu
http://github.com/lab11
Prabal Dutta
http://eecs.umich.edu/~prabal