## Slide 1: MBus: Enabling the Next Generation of Sensors and Systems
Pat Pannuto, Ye-Sheng Kuo, Ben Kempke, Yoonmyung Lee, Zhiyoong Foo, David Blaauw, Prabal Dutta
University of Michigan

## Slide 2: How do you build an embedded system?
Goal: Build a “Temperature Sensor”

## Slide 3: How do you build an embedded system?
Goal: Build a “Temperature Sensor”
Step 1:
  Buy a temperature sensor

## Slide 4: How do you build an embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Buy a temperature sensors
Step 2: Add a microcontroller

## Slide 5: How do you build an embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Buy a temperature sensors
Step 2: Add a microcontroller
Step 3: Add a display

## Slide 6: How do you build an embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Buy a temperature sensors
Step 2: Add a microcontroller
Step 3: Add a display
Step 4: Add a radio

## Slide 7: How do you build an embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Buy a temperature sensors
Step 2: Add a microcontroller
Step 3: Add a display
Step 4: Add a radio
Step 5: Put it all together

## Slide 8: How do you build an embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Buy a temperature sensors
Step 2: Add a microcontroller
Step 3: Add a display
Step 4: Add a radio
Step 5: Put is all together
Step 6: Plug it in.

## Slide 9: How do you build an embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Buy a temperature sensors
Step 2: Add a microcontroller
Step 3: Add a display
Step 4: Add a radio
Step 5: Put is all together
Step 6: Plug it in.
This is how you built an embedded system in 1980

## Slide 10: Modern Technology “Cut the Cord”

## Slide 11: How do you build a low-power embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Buy a low-power temperature sensor

## Slide 12: How do you build a low-power embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Buy a low-power temperature sensor
Step 2: Buy a low-power microcontroller

## Slide 13: How do you build a low-power embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Buy a low-power temperature sensor
Step 2: Buy a low-power microcontroller
Step 3: Outsource the display

## Slide 14: How do you build a low-power embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Buy a low-power temperature sensor
Step 2: Buy a low-power microcontroller
Step 3: Outsource the display
Step 4: Add low-power communication

## Slide 15: How do you build a low-power embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Buy a low-power temperature sensor
Step 2: Buy a low-power microcontroller
Step 3: Outsource the display
Step 4: Add low-power communication
Step 5: Put it all together

## Slide 16: How do you build a low-power embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Buy a low-power temperature sensor
Step 2: Buy a low-power microcontroller
Step 3: Outsource the display
Step 4: Add low-power communication
Step 5: Put it all together
Step 6: Add a battery

## Slide 17: How do you build a low-power embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Buy a low-power temperature sensor
Step 2: Buy a low-power microcontroller
Step 3: Outsource the display
Step 4: Add low-power communication
Step 5: Put it all together
Step 6: Add a battery
This is how you build an embedded system today

## Slide 18: What does the next generation system look like?

## Slide 19: What does the next generation system look like?
To understand the future, look to the past
?

## Slide 20: Cutting the cord let us put intelligence in more places

## Slide 21: What niche does the next generation fill?
“Ubiquitous Computing”

## Slide 22: Why don’t we have ubiquitous computing already?
Paid a heavy cost:
  Batteries gave nodes a lifetime

## Slide 23: Batteries Dominate Node Volume

## Slide 24: A new class of power emerges
“Next Generation” nodes will have
power budgets at or below 1 μW

## Slide 25: How do you build an ultra-low power embedded system?
Goal: Build a “Temperature Sensor”

## Slide 26: How do you build an ultra-low power embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Build an ultra-low power temperature sensor
~10 pW standby, < 1 μW active

## Slide 27: How do you build an ultra-low power embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Build an ultra-low power temperature sensor
Step 2: Build an ultra-low power microcontroller
~1 nW sleep, ~1 μW active

## Slide 28: How do you build an ultra-low power embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Build an ultra-low power temperature sensor
Step 2: Build an ultra-low power microcontroller
Step 3: Outsource the display
Step 4: Add ultra-low power communication
~10 pW standby, ~5 μW active

## Slide 29: How do you build an ultra-low power embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Build an ultra-low power temperature sensor
Step 2: Build an ultra-low power microcontroller
Step 3: Outsource the display
Step 4: Add ultra-low power communication
Step 5: Put it all together?

## Slide 30: How do you build an ultra-low power embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Build an ultra-low power temperature sensor
Step 2: Build an ultra-low power microcontroller
Step 3: Outsource the display
Step 4: Add ultra-low power communication
Step 6: Add power
Energy Harvesting Energy Storage

## Slide 31: How do you build an ultra-low power embedded system?
Goal: Build a “Temperature Sensor”
Step 1: Build an ultra-low power temperature sensor
Step 2: Build an ultra-low power microcontroller
Step 3: Outsource the display
Step 4: Add ultra-low power communication
But How To Put It All together?
Step 6: Add power
Energy Harvesting Energy Storage

## Slide 32: Composing ultra-low power systems: Why not open collectors?
I2C, CAN, SMBus…
Pros
  Multi-master
  Low wire count (~2)
Cons
  Pull-up resistor burns power (order μW)
  Speed / power tradeoff

## Slide 33: Composing ultra-low power systems: Why not “pure digital” buses?
SPI
Pros:
  Single-ended
  Low (no) ACK overhead
Cons:
  Single master
  3 + N wires, N is chip count
    Wires can dominate size
  No ACK mechanism

## Slide 34: We built a new bus (and we actually needed it)
MBus
Pros:
  Multi-master
  Single-ended
  Low wire count (4)
  Reliable reset mechanism
  Low ACK overhead
Cons:
  Topological Priority
MBus System Topology

## Slide 35: MBus Enables ultra-low power systems
MBus is a power-aware bus
So we can build power-oblivious systems

## Slide 36: Ultra-low power computing turns things OFF
How are ultra-low power chips ultra-low power?
They turn OFF (power gating)

## Slide 37: Global State is Hard – So Don’t Do It
MBus guarantees message reception regardless of target chip power state
Power-aware bus

## Slide 38: MBus Insight: Waking Nodes
During arbitration, a node is either:
  Awake or asleep
Sleeping nodes will never arbitrate

## Slide 39: MBus Insight: Interrupt Procedure
In normal operation, DATA is always slower than CLOCK
Extremely reliable
  “Independent” circuit

## Slide 40: So how DO you build an embedded system?
MBus

## Slide 41: MBus enables modular construction of ultra-low power systems
2 uAh Battery
5 uAh Battery
Decap
Control/
PMU
Temp Sensor
Radio
+ CDC
Motion Detection/ Imager
Pressure Sensing
Temp. Sensing
MEMS
P. Sensor
Visual Sensing
MBus

## Slide 42: The “modules” that made MBus possible
Pat Pannuto
Ye-Sheng Kuo
Ben Kempke
Yoonmyung Lee
Zhi Yoong Foo
Prabal Dutta
David Blaauw

## Slide 43: How do you build an ultra-low power embedded system?
?

## Slide 44: How do you power an ultra-low power embedded system?
?

## Slide 45: How do you power an ultra-low power embedded system?
?

## Slide 46: How do you power an ultra-low power embedded system?
?

## Slide 47: How do you power an ultra-low power embedded system?
?
Answer: Build an efficient energy harvester
130 nm Solar Array

## Slide 48: How do you build an ultra-low power embedded system?
?

## Slide 49: How do you build an ultra-low power embedded system?